DRAFT - 10/27/2008

| DATE: | October 31, 2008 |
| --- | --- |
| TO: | Lamprey Technical Workgroup |
| FROM: | Ray Hartlerode, Fish Screening Oversight Committee (FSOC) Chair |
| SUBJECT: | Questions Regarding Lamprey and Screening Facilities |

The Fish Screening Oversight Committee (FSOC) is aware of the need to protect lamprey as well as salmonids at screening facilities, but realizes that expertise on lamprey passage within the FSOC is limited. The FSOC therefore requests that the Lamprey Technical Workgroup review the following initial questions and assumptions regarding lamprey, and provide the FSOC with a summary of available and related information.

- What is known about lamprey attachment and detachment from screens?  What are the impacts of different cleaning mechanisms?

The tribal restoration plan seems to address only the macrophthalmia at screen sites and the impact that a cleaning system might have should they reside on the screen.  The cleaning system in question typically applies to flat plate screens and consists of a single brush or numerous (gang) brushes.  The plan suggests modifications including spray or bubble devices “that would cause lamprey to detach from the screens.”  At sites without power this isn’t an option, especially remote sites.

At rotary drum and traveling belt screen sites the same issue is present sans the cleaning device issue.  If lamprey were to attach to the screen material and were carried vertically, would they detach as soon as they were lifted out of the water?

- Are the current mesh size and approach velocity criteria adequate for various life stages of lamprey?

Sweeping velocity should be high enough to discourage temporary residency and sweep lamprey directly into the bypass.  Currently, the criteria stipulates, “The sweeping velocity shall equal or exceed the maximum allowable approach velocity.”  Does this need to be more specific to accommodate the needs of macrophthalmia?  Of equal if not greater concern is the ammocoete phase. Current criteria mesh size may not be small enough to preclude entrainment of young ammocoetes.

- Is information available regarding swimming strengths (including burst speed as well as sustained speed) of the various life stages of lamprey?

- Can any stage in lamprey life history burrow below a screen structure?

A concern is the potential for ammocoetes to burrow into the canal sediment in front of the screen.  When lamprey are observed on the downstream side of a screen it is assumed that the screen did not work, the screen material was large or there was a gap allowing them to get through.  Is it possible that the screen worked as designed but the lamprey took a path through substrate?

- What is the de-watering rate necessary to protect ammocoetes?

At fall shut-down canals are typically dewatered, unless stock water is provided throughout the winter.  Any lamprey in the canal could then be stranded and lost.  Ammocoetes are susceptible to pressure changes and should emerge during a ramped down dewatering.

- Is the strength of common electrofishers used for juvenile salmonids (e.g. Smith-Root model-12) detrimental to ammocoetes?

If water remains in the canal for some reason, electrofishing typically occurs to salvage any remaining juvenile salmonids.  Ammocoetes are also susceptible to electrofishing and will emerge.  There appears to be one specific model that is used nationally for ammocoete research; model AbP-2™ backpack electrofisher (Engineering Technical Services, University of Wisconsin).

Another concern is the periodic dredging of the canal by the irrigator to reduce sediment load in front of the screen.  If the dewatering isn’t ramped down and/or the canal electrofished prior to dredging activities, ammocoetes will be lost.

- Is information available to indicate operation procedures to minimize effects of screening facilities on all life stages of lamprey?

This may be related to migration timing and biology.

- To what extent are diversion structures barriers to adult lamprey?

We know that some of the diversion structures are currently barriers to salmonids during certain times of the year.  During the design of fishways in the future, lamprey passage should be a consideration.

H:\WORK\AFAC\2008_1104\MemoTo_LTWG_fromFSOC_RevisedDraft102708.doc

.

# Text boxes

851 SW Sixth Avenue, Suite 300 | Pacific First Building | Portland, OR 97204-1339 |

Phone: 503-229-0191 | Fax: 503-229-0443 | www.cbfwa.org

Coordinating and promoting effective protection and

restoration of fish, wildlife, and their

habitat in the

Columbia River Basin.

The Authority is comprised of the following tribes

and government agencies:

Burns Paiute Tribe

Coeur d’Alene Tribe

Confederated Salish and Kootenai Tribes

of the Flathead Reservation

Confederated Tribes

of the Colville Reservation

Confederated Tribes

of the Umatilla Indian Reservation

Confederated Tribes

of the Warm Springs Reservation

Confederated Tribes and Bands of the Yakama Nation

Idaho Department

of Fish and Game

Kootenai Tribe

of Idaho

Montana Fish, Wildlife and Parks

National Marine Fisheries Service

Nez Perce Tribe

Oregon Department

of Fish and Wildlife

Shoshone-Bannock Tribes of Fort Hall

Shoshone-Paiute Tribes of Duck Valley

U.S. Fish & Wildlife Service

Washington Department of Fish

and Wildlife

Coordinating Agencies

Columbia River

Inter-Tribal Fish Commission

Upper Columbia

United Tribes

Compact o the Upper Snake River Tribes