ISRP Comment/Question: Delay funding until a watershed assessment is complete and a site plan and systematic evaluation of the limiting factors to justify the activities has been prepared.

Response: This criticism, while valid, fails to take into account the realities of the funding cycle. The deadline for submission of FY 2000 proposals was December 1998, when the assessment had just been initiated. Thus, even though the project sponsors were well aware that problems affecting steelhead habitat exist in the upper Toppenish/Simcoe watershed, they were not able to provide specifics. Practicality and efficiency dictate that watershed restoration activities maintain continuity while a backlog of restoration work exists, as it is infeasible to annually disassemble and reassemble crews with the necessary knowledge and experience.

Completion of the watershed assessment has been delayed, primarily by the unusual depth and persistence of the snowpack accumulated over the winter of 1998-99. The upper segments of the watershed became accessible only in June. A Riparian Proper Functioning Condition Assessment (PEC) (USD1 Bureau of Land Management, 1993. TR 1737-9) has been performed on the lower- to middle reaches of Toppenish, Branch, Willy-Dick, Agency, Wahtum, and Simcoe creeks, and a number of headwater meadows that are source areas for summer baseflows have been surveyed.

Generally, the PEC findings parallel those in the Satus watershed, i.e., stream system degradation increases in the downstream direction. This trend is the result of both cumulative effects and stream type. The higher mountain streams are generally more geologically controlled (confined), and therefore less susceptible to disturbance from human activities. Where the streams are less confined they are generally incised and disconnected from their floodplains. The notable exception to this trend is the mainstem of Toppenish Creek, from the confluence of the North Fork Toppenish, downstream to the Toppenish Lateral Canal. This reach, occupying a relatively wide canyon, is in proper functioning condition, despite the February 1996 flood of record.

Channel incision and loss of floodplain function cause serious, long-term impairment of hydrologic functioning. Much of the stream network involved is composed of dynamic, high-gradient, cobble-bedded, canyon reaches. Banks and floodplains are generally composed of a cobble matrix, with fines filling the interstices. This characteristic indicates the high-energy nature of the water and sediment processing in the intermediate elevations of the watershed. Under these conditions, channel incision is difficult and slow to reverse, and recovery can be set back by either excessively high flows or drought. Active restoration in this part of the stream system will be slow, costly, and at high risk of failure, and should be deferred in favor of flow-moderating activities higher in the watershed. Any moderation of flows will benefit the entire downstream system and increase the chances for recovery.

Current causes of degradation of the stream system in the upper watershed are predominantly related to the road system and grazing management. FEMA-funded flood damage road repairs and road improvements funded by timber sale revenues have begun, and the project sponsors are providing technical support to ensure that these projects have results beneficial to the fisheries resource. These projects address the big ticket’ items along the main routes in the upper watershed. A large number of smaller-scale road drainage problems affecting streams along the secondary roads of the upper watershed will be addressed. These problems include faulty culvert placement, and eroding cut banks and ditches. The means for addressing these problems are straightforward: culvert repositioning or replacement, cut slope re-vegetation, ditch relief, sediment trapping. The closure and rehabilitation of roads will also be pursued wherever possible, especially those encroaching on floodplains. Road rehabilitation will involve culvert removal, water barring, ripping and seeding.

Several headwater meadows have been surveyed on the Lincoln and Lost Horse plateaus that are being degraded by roads and poorly managed grazing. The most serious road problems involve culverts installed be1ow grade. These culverts have lowered the base level of the drainage system, causing headcutting, channelization, and loss of water storage capacity. The project sponsors intend to reestablish the previous base levels by repositioning the culverts, or by installing fords, depending on specific site conditions. Further degradation will be arrested by stabilizing headcuts with combinations of rock, geotextiles, and vegetation.

Grazing management will be improved by working with the grazing permit holders to implement rotational grazing systems and develop off-channel watering facilities and corrals. Currently work is coordinated with one permit holder to develop a cattle trail that will enable him to quickly move his cattle past a number of sensitive riparian areas during the initial spring turnout, and again during fall gathering.

ISRP Comment/Question: Objectives were stated in terms that were measurable, but they were primarily focused on structural changes in habitat.  These are easier to measure in the short-term than population characteristics, but ultimately the success of the project must be judged by increases in the production, distribution, and diversity of fish in the watershed.

Response: Yakama Nation Fisheries Program staff has monitored steelhead in Toppenish Creek since 1989, and continue to do so. This is valuable information that helps prioritize restoration activities. However, anadromous fish populations are not the appropriate measure of the effectiveness of these restoration treatments.  This watershed restoration proposal is based on the premise that healthy watershed functioning provides the watershed attributes valued by the Tribe, including fish habitat. Due to the effects of environmental conditions outside the watershed, in combination with naturally occurring disturbances within the watershed, anadromous fish population data do not measure the effectiveness of restoration treatments.