Project ID: 20122

Test guidance flows and strobe lights at a SBC to increase smolt FCE & FGE

Washington Department of Fish and Wildlife

Short Description:  Test guidance flow and strobe lights at the Cowlitz Falls Dam to increase FCE and FGE. Radio telemetry, fyke and flume nets and facility collection will be used to measure the success of guidance flow and strobe lights.

ISRP Recommendation - Fund in Part / CBFWA Tier 3 / ISRP Comparison with CBFWA: Disagree - fund in part

Sponsor Funding Request = $295,000 / CBFWA Funding Recommendation =

Recommendation:

Fund in part with emphasis on testing guidance flow.

Comments:

Authors offer an excellent presentation of a project with a good experimental design and monitoring provisions, and with encouraging prospects for success.  They demonstrate a very good understanding of downstream fish passage issues, and do a good job relating this work to regional programs and needs.

The proposal provides an adequate explanation of the guidance flow portion of the experiment, but neglects to relate where strobe lights would be placed and how they would be employed in the experimental phase.  Neither does it indicate how environmental conditions would be monitored.

Specific questions and comments that should be addressed are:

Would strobe lights always be used in conjunction with the attraction flows, or would the two techniques be tested separately?  The proposal alludes to the prospect that additional funding may be obtained from Tacoma Public Utilities.  If so, how much, at what time, and how would the money be spent?

Response:   We note the general placement of strobe lights on page 12, Section 8.a.5. “Strobe lights placed in the entrance to the induction slots would deter smolts from entering and divert them away from the induction slot and provide them the opportunity to discover and cue in on the guidance flows to the collection flumes.”

Three sets of three strobe lights would be located at or adjacent to the entrance to the induction slot and mounted on the grated slot covers of each induction slot.  The entrance to the induction slot is located about 10.5 meters below normal reservoir operating level.  The induction slot is about 2.5 meters across (front to back, upstream/downstream) and 6.5 meters across.  The concrete floor (ogee) from the baffle panel (upstream) to the spill gate(downstream) angles upward at about a 45 degree angle.  The front edge (upstream) of the grated slot cover is about 3 meters behind the baffle panel. The strobe lights will be powered from a control panel on the deck of the dam.  The control panel offers the ability to adjust both flash rates and light intensity.  The settings and final placement of the strobe lights, once chosen, would not change during the course of the study.

Operation of the strobe lights would be embedded in a statistical randomized block design with on and off treatments.  A statistician experienced with fish passage studies and projects will guide final study design (noted on page 16, Section 8.f.1.).  A key criteria for the final design will be to assure that the study design does not lead to confounding data and results between the strobe light and directed flow components.   The design must provide the ability to identify fish response to each component separately.  As part of the experimental design, lights and directed flow components may be on at the same time, but only if we can address the success of each component independently.  It’s also important to recognize that we view the two components as part of a system that work together to improve guidance and collection.  The strobe lights to deter smolts from entering the induction slots and guide them upwards to increase the likelihood of them sensing the directed flow currents within two the three meters of the surface and into the SBC..

On page 4, Section 4. We note under objective 2. that we will “Determine how environmental conditions effect guidance flows and/or strobe light guidance; i.e. diel patterns, turbidity, and flow” and as objective tasks “a.  Measure reservoir turbidity and correlate to strobe light effectiveness, b.  Monitor day vs. night responses using data from task #’s 1c,1d and 1e.”

More specifically we would measure and record turbidity with a secchi disk,  HACH Turbidity meter and measure light intensities with an electronic light measuring device (radiometer/photometer e.g. IL1400A, International lights Inc.) to relate to collection and guidance data.  We note on page 16, Section 8.e.1.2. that “We will assess how environmental conditions effect strobe light efficacy; i.e. diel patterns, turbidity and flow.  If feasible turbidity and flow may be incorporated into the statistical analysis as covariates.”.

Tacoma Public Utilities (TPU) has not made any commitments to provide additional funding for this project.  However TPU did contribute to on-going work at the Cowlitz Falls Project in 1999 with the purchase of 200 Lotek radio tags.  If this proposal is funded we would ask TPU to provide 200 additional radio tags to strengthen the study design and analysis.  If TPU chooses to purchase additional radio tags, we would expect them to order the tags directly from Lotek in the early spring of 2000.   This would represent a contribution of more than $40,000 to the project.

Submitted by:

Charles Morrill

(360) 902-2747

Washington State Dept. of Fish and Wildlife

June 22, 1999