# Bonneville Power Administration

# FY 2001 Innovative Project Proposal Review

# PART 2 of 2. Narrative

Title:	Ultrasonic Induced Sonochemical Destruction of Pathogens, Viruses, Nitrates and Other Nutrients and contaminants From Waste Discharge Streams

a. Abstract

Laboratory tests have shown that ultrasonic induced cavitation is a low cost of method of destroying organisms and contaminates in water.  This innovative process promises to replace existing technologies with a treatment system that is of low maintenance, low power costs, and does not generate either secondary aqueous waste streams or materiel to be disposed.

This proposed project consist of constructing and installing a 600 gallons per hour treatment pilot plant, using Water Services, L.L.C. proprietary technology.  The pilot plant will be installed at the headworks of a fish hatchery presently concerned with the quality of water entering the plant for half of the test period.  For the second half of the test period the equipment will be located at the outfall side of the hatchery.  The first site of the pilot plant will be upstream of existing ultraviolet treatment facilities.  The second placement will be just before final disinfection before entering the river.  In this manner the pilot plant will be able to provide required information but will not interfere with the current operations of the hatchery.

The plant will be monitored continuously during its operation.

b. Technical and/or scientific background

The basic methodology of contaminate removal from wastewater streams has used essentially the same unit operations for many decades.  Some of the more significant developments in wastewater treatment have been the commercial realization of synthetic membranes for reverse osmosis and ultrafiltration operations.  Also of great benefit was the appearance of waste effluent treatment with UV enhanced oxidation.  However, with the use of synthetic membranes pretreatment (sometimes extensive) is required to maximize the service life.  Although synthetic membranes have been optimized for product flux, a secondary waste stream is generated in the form of a concentrated reject.

The use of UV enhanced oxidation has its own set of requirements for optimal performance.  For example, the quartz tubes must be maintained to optimize the UV flux into the waste stream and a continuous feed of an oxidizer (such as ozone) must be supplied.

Water Services, through the use of proprietary design, has optimized the influence of cavitation induced sonochemistry effects in the bulk solution.  This design has allowed Water Services to treat wastewater in a continuous unit operation versus a batch reactor.

Analytical results from a single pass treatment (not optimized as to residence time) of potato wastewater indicate a  reduction in the chemical oxidation demand of approximately 98%, and a likewise reduction in the biochemical oxygen demand.  However, unlike the above mentioned advanced treatment technologies, the Water Services’ technology will reduce total nitrogen one order of magnitude.  It is also anticipated (through scouting tests) that the nitrate is decomposed within the treatment unit to nitrite and nitrous oxide.

Cavitation refers to the formation and subsequent dynamic life of bubbles in a liquid medium.  The bubbles may be filled with either gas or vapor and form under a variety of conditions.  Traditionally, cavitation is referred to as either transient or stable.  Transient cavitation involves large-scale variations in the bubble’s size (relative to its equilibrium size) over a time scale of a few acoustic cycles.  Stable cavitation usually involves small-amplitude (as compared to the bubble’s radius) oscillations about an equilibrium radius [1].

When cavitation occurs and subsequent bubbles collapse the chemical reactions occur through sonochemistry and sonoluminescence.  The collapsing bubble elicits some very dramatic and localized conditions at the loci of collapse, which has a direct effect upon molecular species.  For example,  the chemical effects of ultrasound do not come from a direct interaction with molecular species. Instead, sonochemistry and sonoluminescence arises from acoustic cavitation: the formation, growth, and implosive collapse of bubbles in a liquid. Cavitational collapse produces intense local heating (~5000 K), high pressures (~1000 atm), and enormous heating and cooling rates (>10 9 K/sec). Acoustic cavitation provides a unique interaction of energy and matter, and ultrasonic irradiation of liquids causes high energy chemical reactions to occur, often accompanied by the emission of light [2].

According to Suslick, the following graphical representations indicate both the energies of cavitation (Figure 1) and the bubble radius (y-axis) versus time to collapse (Figure 2).

Figure 1

Figure 2

The subsequent effect upon water, inorganic species, and organic species has been investigated.  In the sonolysis of water, researchers have provided evidence for the intermediacy of OH(, H( along with high energy species eaq(, and (HO)2( [3,4,5].  It is important to note that the literature cited below generally used sonication in the 20 KHz range.  This frequency is far below that used by Water Services in their water treatment unit.

Table 1 addresses the principal products of a few inorganic species:

Table 1

| Aqueous Sonochemistry of Inorganic Compounds |
| --- |
| Substrate Present | Principal Products | Reference |
| Br( , Cl( | Br2, Cl2 | 6, 7 |
| [NO3]( | [NO2]( | 8 |
| H2S | H2 + S8 | 9 |
| Fe2+ | Fe3+ | 10 |

As to organic degradation, there have been numerous studies indicating the success of cavitation induced sonochemistry.  Weaver, et. al, demonstrated the destruction of pentacholorphenol with aromatic intermediates (tetra-choloro-o-benzoquinone and tetrachlorocatechol) that were also destroyed via sonochemistry in the laboratory reactor .  However, when sonolysis coupled with ozonation was used, the aromatic intermediates were not detected [11].

Researchers have shown the degradation of organic compounds such as carbon tetrachloride, 1,4-dioxane, and polychlorinated biphenyls [12, 13, 14].  Each of the authors indicated intermediate products were formed.  Water Services unit operation, in addition to the ability to maintain cavitation and sonochemistry in the bulk solution with a continuous reactor, also will maintain the residence time to destroy intermediate products formed during organic degradation.

Initial scouting tests with the Water Service unit have indicated that organic destruction occurs (reduction in BOD and COD) as well as a decrease in nitrate concentrations.  We propose that this unit will find benefit in the tertiary treatment of wastewater (replacing chlorination) before release into the environment, which will also disinfect aqueous streams containing microbes [15, 16].  With the ability to realize organic destruction, Water Services also proposes that the unit will be able to successfully treat organically contaminated groundwater at a well head before the water treatment plant.

c. Rationale and significance to Regional Programs

Water quality at hatcheries, both influent and effluent, is a vital  factors in the health of Colombia Basin salmonoids.  Native stock and hatchery fish are affected by poor water quality at hatchery sites and the impact of contaminated water can be devastating to existing fish and recovery efforts.  The NMFS Draft Biological Opinion states, in section 5.3.3, “Ecologically, hatchery fish can increase predation on, displace, and/or compete with wild fish.  These effects are likely to occur when fish are release in poor condition and do not migrate to marine waters…  Hatchery fish also may transmit hatchery-borne diseases, and hatcheries themselves may release diseases into streams via water effluents”.  Influent water must be of such a quality that allows for the growth of healthy stock, and the effluent must not contain any organisms that can be transferred to the resident population of fish.

Present water treatment technology relies on filtration, disinfection and sometimes reverse osmosis to achieve desired water quality.  These methods are expensive to install, operate and maintain.  And, often the systems do not meet required standards because of  the difficulty of maintaining proper maintenance schedules, changes in raw water character or equipment failures.

Hatchery production of salmonoids is an important part of the species recovery program, as evidenced by Section 7, Coordinated Salmon Production and Habitat, of the Fish and Wildlife Program.  The Council is dedicated to improving existing hatchery production without negative impacts on wild fish.  Water quality at the hatcheries is essential to production of healthy fish, and reduction of the possibility of disease entering any portion of the Columbia Basin.

The Water Services ultrasonic cavitation process, while complex from a chemical standpoint, is simple.  The proof of concept machine, which treats 6000 gallons per hour, Is of solid state construction, and has few moving parts.  The electrical requirements are approximately 10kw per hour, which would cost out to about $83.00 to treat one million gallons of water.  The unit is self monitoring and will automatically shut down and/or call for service if a problem develops.  All this means that the equipment can be placed at intake locations to provide treatment of water entering the hatchery, and at the outfall, to destroy any organisms that may carry disease to native species.

d. Relationships to other projects

The proposed project would have a direct relationship on hatchery practices and operations to preclude the introduction and/or spread of any fish disease within the Columbia Basin.  The water treatment system would maximize the health of fish released from hatcheries by ensuring that the influent water is free of deleterious organic compounds, microbial and viral pathogens.  The effluent from the hatcheries would be treated to ensure that receiving waters would not be subjected to high BOD loadings or fish diseases.

e. Proposal objectives, tasks and methods

Objectives

The primary objective of this effort will be to delineate the residence time through the cavitation induced sonochemical water treatment unit (CISWTU) for appropriate log reductions in microbial colony forming units, virual plaque forming units, and organic compounds such as pesticides.  Once the optimal residence time is determined for each group of interest, then an influent stream containing all chemicals and microbial concentrations of interest will challenge the CISWTU.

To support the primary objective the following will be accomplished:

Objective 1.  Delineate the organic compounds and biologicals of interest to the fish hatchery efforts at the BPA.  Agree upon a statistically defensible experimental design for challenge influents to the CISWTU.

Objective 2.  Challenge the CISWTU with organic compounds (such as pesticides) and the biologics of concern at known concentrations using chlorine-free groundwater.  The challenges will use concentrations of each organic and/or biologic of concern at first.

Objective 3.  Challenge the CISWTU will the upper level concentrations of the all organics and biologics of concern as a single influent.  The challenge will be continuous over a period of time to attain continuity of water quality.

Objective 4.  The CISWTU will be sited at a fish hatchery and plumbed to receive both influent and effluent (at different times) from the fish hatchery.  The unit will run continuously over a minimum of 30 days to attain water quality and cost information.

Tasks and Methods

Task 1:  Organic Compounds and Biologicals of Interest.

Subtask 1.1:  Meet with BPA Hatchery personnel to form a consensus of organics and parasites (microbial, viral, and protozoan) of interest.

Subtask 1.2:  Submit an experimental design to statistically address challenge of the CISWTU with agreed upon contaminants (organic and biological) from Subtask 1.  The design will be a factorial to determine the optimal flow rate, resonance frequency, and residence time required to achieve the desired destruction.

Task 2:  Challenge of the CISWTU using the protocol from Subtask 1.2.

Subtask 2.1  Organic Challenge:  The agreed upon organics will be used to challenge the CISTWU individually at several concentrations each.

Subtask 2.2  Biologic challenge:  The unit will be challenged using bacteria and bacteriophages (surrogate for viruses) at several concentrations.

Analysis Methods:  For organics, the use of Standard Methods for the Examination of Water and Waste Water will be used.  For biologics, standard plate count techniques and bacteriophage assay techniques will be used.  The offgas will be monitored and analyzed using standard methodology.

Task 3: Continuous challenge of the CISWTU:  Figure 1 is a schematic of the envisioned continuous challenge mode for the CISWTU.  The untreated influent will be made up in Tank A, with continual recirculation to achieve continual mixing.  The CISWTU will treat the challenge water and offgas samples will be taken during the course of each run.  Tank B will hold the treated effluent (Two tanks will be used, not shown) and after analysis indicates contaminate levels, the effluent will be discharge to an appropriate receiving unit.

Figure 1

Task 4.   Siting of the CISWTU:  The unit will be skid mounted and sited at a chosen fish hatchery.  The unit will be operated continuously over a thirty day period.  In-line monitoring will be accomplished to the extent possible (depending upon contaminates of concern identified by hatchery personnel).  For all other analysis, an independent laboratory will be used as close to the site as geographically possible.

Task 5.  Report:  Water Services, LLC., will provide monthly reports to the BPA, a six month report and a final report, 30 days after the study is completed.

f. Facilities and equipment

Water Services, LLC. Will provide the CISWTU, floor space and analytical capabilities for Tasks 1, 2, and 3.  For Task 4, Water Services will provide a skid mounted unit, transport the unit, mobilized the unit at the selected hatchery, operate the unit for the requisite time period, demobilize the unit, and transport the unit back to the Nampa, ID, facility.

g. References

- Atchley, Anthony A. and Lawrence A. Crum, in Ultrasound, its Chemical, Physical, and Biological Effects, Kenneth S. Suslick, ed., VCH Publishers, Inc., 1988.

- K.S. Suslick in Kirk-Othmer Encyclopedia of Chemical Technology; 4th Ed. J. Wiley & Sons: New York, 1998, vol. 26, 517-541.

- Riesz, P.; D. Berdahl; C. L. Christman; Environ. Health Perspect. 1985, 64, 233.

- Margulis, M. A.; A. N. Mal’tsev; Zh. Fiz. Khim. 1968, 42, 2660.

- Margulis, M. A.; A. N. Mal’tsev; Zh. Fiz. Khim. 1972, 46, 2970.

- Margulis, M. A.; A. N. Mal’tsev; Zh. Fiz. Khim. 1968, 42, 1441.

- Gueguen, H.; Ann. Chim. 1963, 8, 667.

- Margulis, M. A.; Zh. Fiz. Khim. 1974, 48, 2812.

- Cauwet, G.; C. M. Coste; H. Knoche; J. P. Longuemard; Bull. Soc. Chim. Fr. 1976, 45.

- Sehgal. C.; R. G. Sutherland; R. E. Verrall; J. Phys. Chem. 1980, 84, 2920.

- Weaver, L. K.; N. Malmstadt; M. R. Hoffmann; Environ. Sci. Technol. 2000, 34, 1280.

- Hua, I, M. R. Hoffmann; Environ. Sci. Technol. 1996, 30, 864.

- Beckett, M. A., I. Hua; Environ. Sci. Technol. Elucidation of the 1,4-dioxane Decomposition Pathway at Discrete Utrasonic Frequencies, Accepted for publication June 29, 2000.

- Zhang, G.; I. Hua; Environ. Sci. Technol. 2000, 34, 1529.

- Phull, S., T. J. Mason, J. P. Lorimer, A. Newman, and B. Pollet, Ultrasonics, 1997, 4, 157.

- FWR Research Report, Applications of Ultrasonics in the Water Industry, 1995.

# Section 4. Key personnel

James B. Duncan, Ph.D.,  Principal Investigator

### EDUCATION

Doctor of Philosophy, Civil (Environmental) Engineering, Texas Tech University, 1985

### AFFILITIONS

American Institute of Chemical Engineers

North American membrane Society (Board of Directors, 1987 – 1989)

New York Academy of Sciences

Sigma Xi

Water Environment Federation

### EXPERIENCE –

Experience 1992 – to Present

Idaho National Engineering and Environmental Laboratory

Clean Closure of V-Tanks in Operable Unit 1 (Waste Area Group 1, Test Area North) – Brought technical points to the team as to why in-situ vitrification should not be the remedy of choice in the ROD.  Identified vendors to treat the waste and disposal options.  Due to the surfacing of technical concerns, an alternative pathway was chosen saving the taxpayers approximately 8 million dollars.

Proposal For Demonstration of Innovative Water Treatment Technology – Major contributor for a proposal to demonstrate efficacy of an INEEL proprietary water treatment process aimed at treating water for Cryptospodrium without chemicals.  The INEEL is teamed with two commercial engineering firms to bring the technology forward.

COGEMA Engineering Corporation (Formerly Westinghouse Hanford Corporation)

Flowsheet Development for the Hanford Tank Initiative Program, Clean Closure of AX Farm Underground Storage Tanks

K Basin Spent Nuclear Fuel (SNF) Stabilization Program Tank Waste and Retrieval System, Privatization Program Proton Storage Ring (PSR) Program, Los Alamos National Laboratory

Effluent Treatment Facility (ETF) Program, Hanford

N Basin Spent Nuclear Fuel (SNF) Pool Stabilization Program

KR-4 Pump and Treat Project.

N Basin Potable Water Tank Focus Area Program

Efficient Separations and Integration Program

Hanford 100 Area CERCLA Activities

Adjunct Faculty, Department of Civil and Environmental Engineering, Washington State University

Experience 1991 to 1992:

Pacific Northwest National Laboratory

Staff Engineer, Waste Technology Center

Experience 1986 to 1991:

Eastman Kodak Company

Manager, Advanced Chemical Technologies (ACT) Group, Eastman Kodak Experience 1980 to 1985:

Commissioned Officer, US Army Chemical Corps.

.

Harry Beaulieu Ph.D.., CIH,CSP

EDUCATION

Ph.D., Environmental Health, University of Okalahoma, 1976

M.S., Environmental Health, University of Minnesota, 1973

B.A., Biology/Chemistry, University of Minnesota-Morris, 1972

CERTIFICATIONS

1979 – Certified Industrial Hygienist (ABIH), #1646

1978 – Certified Safety Professional (BCSP), #5819

1987 – Asbestos Project Designer Training Course (AHERA)

1991 -  Certified Instructor, 30 CFR (Part 48) MSHA

- -  Hazardous Waste Operations and emergency Response

AFFILIATIONS

Diplomat to the American Academy of Industrial Hygiene

American Industrial Hygiene (President of Rocky Mountain Section)

EXPERIENCE

1985 to present – President/Laboratory Director, Industrial Hygiene Technologies, Inc.

1983 – 1984, Industrial Hygiene consultant with Safety and Health Consultation Service, Boise State University

1977 – 1982 – Professor of Industrial Hygiene and Environmental Health, Colorado State        University

Lanny G Sloan, P.L.S., Project Administrator

Education

B.S., Business Management, Lewis-Clark State College, Lewiston, Idaho, 1990

CERTIFICATION

Professional Land Surveyor, Idaho Registration #3701, 1979

Certified Grant Administrator, State of Idaho 1988

AFFILIATIONS

American Waterworks Association (Board of Directors, Intermountain Section1988 – 1990)

American Public Works Association

Pacific Northwest Pollution Control Association

Water Environment Foundation

Salmon Basin Advisory Group

EXPERIENCE

1993 – 2000, City Administrator, Salmon, Idaho

1993 - 2000, Owner, Sloan Surveying, Salmon, Idaho

1990 – 1993, Public Works Director, Coos Bay, Oregon

1982 – 1990, Public Works Director, Jerome, Idaho

1981 – 1990, Project Superintendent, Holley Construction

1977 – 1980, Professional Land Surveyor, E-H-M Engineers, Inc., Twin Falls, Idaho

# Comments

Enter project title from Part 1

Describe the project and work to be accomplished. Specifically, describe how the proposal is innovative. Please limit to 300 words.

Clearly identify the problem your innovative project addresses. Describe the background, history, and location of the problem. Include a scientific literature review that covers the most significant previous work history related to the project, including work of key project personnel on any past or current work similar to the proposal. The purpose of the literature review is to place the proposed research in the larger context of what work has been done, what is known, and what remains to be known. All references should be concisely summarized, cited, and listed in section g below

Describe why your innovative project is needed. Specifically, describe the relation of your proposed project both to regional management objectives and to the goals and objectives of the 1994 Fish and Wildlife Program, NMFS Biological Opinion, or other plans. Make a convincing case for how the proposed work will further goals of the fish and wildlife program. Relate project objectives and hypotheses as specifically as possible to the fish and wildlife program objectives and measures or to other plans. Show how the proposed work is a logical component of an overall conceptual framework

Describe the relationships and links between your project and other relevant projects in progress in the Columbia Basin and elsewhere. Put your project into the context of other work funded under the fish and wildlife program. Indicate how your proposed project relates to, complements or includes collaborative efforts with other proposed or existing projects, specifically those in your watershed, subbasin and province. If the proposed project requires or includes collaboration with other agencies, organizations or scientists, or any special permitting to accomplish the work, such arrangements should be fully explained. If the relationship with other proposals is unknown or is in conflict with another project, note this and explain why.

e. Proposal objectives, tasks and methods

Present your project’s objectives, tasks, and methods to implement the tasks (use and expand upon the objectives and tasks from the Budget Tables in Part 1, Section 2). Present these in a numbered list; outline and link by objective, task, and method; and group appropriately to avoid redundancy.

List the ultimate goals, visions, or long-term desires for your project (e.g., increase harvest, restore or maintain or protect a certain population, maintain species diversity, etc) and match these with regional management objectives and strategies. In addition, provide objectives that are measurable in biological terms (e.g., harvest rates at 1 fish/angler/day annually, number of redd counts, population targets) and have a time element (e.g., accomplish by August 2002). Research proposals must concisely state the hypotheses and assumptions necessary to test these. Non-research projects must also state their objectives. In addition to the broad goals and biologically measurable objectives of your project, clearly identify any products (reports, structures, etc.) that would result from your efforts, but be sure to describe the purpose that the products are intended to meet

Under each objective, list the tasks and methods that will be used to meet the objective. Describe how the project is to be carried out based on sound scientific principles (this is applicable to all types of projects). Include scope, approach, and detailed methodology. Indicate how the innovative techniques and methods will further the understanding of fish and wildlife ecology, correct a specific problem in the basin, or broaden and better define the spectrum of management options. Concisely summarize the methods here in enough detail to satisfy peer review and cite references

All major facilities and equipment to be used in the project should be described in sufficient detail to show adequacy for the job. For example, the proposal should indicate whether there are suitable (based on contemporary standards) field equipment, vehicles, laboratory and office space and equipment, life support systems for organisms, and computers. Any special or high-cost equipment to be purchased with project funds should be identified and justified. This section should be no longer than a few paragraphs.

If you have key technical documents specifically related to your project that are cited and summarized in the proposal form, you may submit these as background reference material for the peer reviewers. These documents may include project master plans, monitoring and evaluation plans, watershed assessments, and peer-reviewed articles generated from the project. Please note that the ISRP and CBFWA will evaluate your project based on the proposal, so all critical information needs to be provided in the proposal. Simply referencing another document will not suffice. It is not necessary to send in cited material, but if you do, please note it in the right hand column of the reference table. If your document is available on the web (e.g. through BPA) please provide the web address. If not on the web, but you have an electronic copy please provide it by email or disc. If only available in hard copy send that. Send all materials to the same address you send the proposal form.

Include names, titles, FTE/hours, and one-page resumes for key personnel (i.e. principal investigators, project managers, key subcontractors), and describe their duties on the project. Emphasize qualifications for the proposed work. Resumes should include name, degrees earned (with school and date), certification status, current employer, current responsibilities, list of recent previous employment, a paragraph describing expertise, and up to five recent or especially relevant publications or job completions.

# Text boxes

Tank

A

Tank

B

Recirculation  Pump

CISWTU

Flow Pump

CISWTU

With Offgas