## RESPONSES TO ISRP COMMENTS:  October 12, 2001

## Project ID: 198402500

GRANDE RONDE BASIN FISH HABITAT ENHANCEMENT PROJECT

Sponsor: Oregon Department of Fish & Wildlife

Subbasin: Grande Ronde

Short Description: Protect and enhance fish habitat in selected streams on private lands in the Grande Ronde Basin to improve instream and riparian habitat diversity, and increase natural production of wild salmonids.

FY02 Request: $456,416

3 YR Estimate: $1,438,850

ISRP Preliminary Review Comments:

A response is needed.  This proposal is to continue work on a 15 year old project that includes 40 individual habitat enhancement projects.

The technical background provided in the proposal is again excellent, providing good explanation of the problems and the choice of approaches to address those problems. The project has strong ties with other projects. The project history is thorough and includes summaries of monitoring results. In response to earlier ISRP comments, some evaluation of results is also presented. The examples of monitoring are limited by the types of data presented (i.e., max and min values), but the data have apparently been collected.

Reference is also made to more extensive evaluations in preparation. The discussion of project results and evaluation provides detail on methods to be used to meet the 7 objectives. New monitoring is also described. The adaptive management implications section is quite a good discussion of approaches taken and modified after evaluating results. However, inconsistencies between the proposal and presentation should be reconciled. Although the monitoring plan presented in the proposal is adequate, the responses made during the presentation to questions about monitoring raised questions as to whether monitoring, and especially evaluation, is actually being done.

Response:  The proposal and presentation contained a limited number of examples of monitoring.  We felt the summaries provided in the proposal were adequate, and the presentation was used primarily to illustrate our general approaches to restoration.  Some of the photographs in the “Major Results Achieved” section (pgs 17, 19) and all of the charts and graphs in the Monitoring and Evaluation section of the proposal (pgs 22-25) included data through the year 2000.  Many of the photopoints used in the presentation were collected in 2000-2001 as well.  The 2000 Annual Report to BPA (excerpts are attached as Appendix 1 at the end of these responses, the entire report is attached as a pdf file) includes a section on M&E, which details the monitoring conducted in the year 2000.  Monitoring completed in 2001 has not yet been reported, but is listed separately in this section below.  The monitoring plan in the 2002 proposal was put together after review of numerous ISRP comments on many projects, and after considerable thought and discussions among several state and tribal habitat biologists.  Some additional details of past and current project monitoring are included below:

Stream Temperatures:  The graphs were compiled from hourly temperature data that have been collected 365 days per year, for 10-15 years, and the two examples provided were used to generally summarize what we have found.  Additional graphing/summarization of temperature data along with other monitoring are included in each year’s annual reports to BPA, which are posted on the BPA website (see Appendix I for an example).  Temperature spreadsheets and graphs for each of the 12 stream sites on 6 streams (Meadow, McCoy, Sheep, Salmon, Beaver and Camas creeks) have been collected and summarized dating from 1988 through 2000.  The 2001 data was downloaded in May, and will be downloaded again in November, but is not yet summarized.  Air temperatures were also recorded beginning in 1995.

These data have been regularly reported and distributed to a number of groups including Oregon Department of Environmental Quality, the CTUIR, local SWCD’s and Oregon State University.  Temperature data are summarized as mean weekly maximum and minimum values, which is similar to the method recommended and used statewide by the ODEQ.  Daily maximum and minimum values, by year/month have also been plotted for each site.  Summer data for individual years has also previously been reported in annual reports for other streams (Whiskey Creek, Jordan Creek, Little Beaver Creek, Bowman Creek, and Butcherknife Creek) to help us identify where temperatures are a limiting factor.  Other researchers such as Matthew Boyd of ODEQ who has done extensive temperature modeling, and Dr. Beschta of OSU have reviewed the data and suggested that it would have been more valuable if flows, shade and various channel characteristics had also been collected.  These proposed changes will be incorporated into any new temperature monitoring sites.

Habitat Monitoring Transects:  Transect data were collected for 4 streams dating from 1988 to 2001.  The 1988 data sets are all pre-project data.  Cross section data includes horizontal distances at 1-2 foot intervals, vertical elevations to the nearest 0.05 ft., feature class (floodplain, bank, pool, riffle, etc.), water depth, active and wetted channel widths, instream substrate class (sand, gravel, etc.), riparian cover class (grass, forbs, shrubs, etc.), undercut streambanks, overhanging vegetation, solar pathfinder data and photopoints.

STREAM		Years completed		No. Transects

Sheep Creek 		1988, 1994 and 2000			40

McCoy Creek		1988, 1994, 1997, 2000		40

Chesnimnus Creek	1988, 1994, 2001 (in progress)	30

Elk Creek		1988, 1994, 1997			30

We have only had time/funding to collect, error check and store the majority of the data.  The only summaries we have completed were the solar pathfinder data (shown in the proposal, pg. 23).  As the ISRP suggests, a person with strong quantitative skills will be required to complete data entry, summarization and analysis.  It will take several months to complete the analysis of all 140 transects.  We have not had adequate funding to accomplish this worthwhile task, but would like to do so.  In addition, we would like to compare the methods and results with other habitat evaluations, including the Research & Evaluate Restoration of Northeast Oregon Streams (project No. 200005100) by Kauffman of OSU.

Photopoints:  Several photopoints have been established on each of the 42 projects, and include site maps, descriptions and instructions on how to accurately repeat them.  They are taken annually, some of them dating back to 1986.  Storage of all photopoints is in the ODFW La Grande office, and presently includes about 2,443 individual slides.  Two hundred twenty nine photopoints were repeated in 2000.  Approximately 289 have been established or repeated in 2001.  We compare before/after photopoints each year and note changes in canopy, shading, bank stability, and channel width/depth ratios.  A checklist of the review criteria used in this analysis will be provided in future annual reports.  Approximately 80% of our projects are showing progress toward meeting our riparian restoration objective (Objective 1) and show strong evidence validating our approaches.  Several examples were provided in the proposal and in the presentation.  Addition photopoints (over 50) have been established on instream work sites in the last 2-3 years to document changes in structure alignment or bank stability and other stream channel responses.  Examples of photopoints have been included in past annual and quarterly reports to BPA.  The project biologist compiled a “Before/After” photopoint notebook in 1994 illustrating 22 individual sites with a discussion of various treatment strategies.  A limited number of copies were distributed to interested parties including ODFW district fisheries biologists and the Grande Ronde Model Watershed Program.  These were used when making contacts with landowners interested in new projects to illustrate potential results.  With the ability now to digitize photopoints, a more complete series of photopoint before/after pictures is in progress that can be more widely distributed, but will not be available until 2002.  In addition, we are investigating the possibility of making future photopoints more quantitative using the methods outlined in the “Photo Point Monitoring Handbook”, USDA/PNW Gen. Tech. Rep. by Frederick C. Hall (2001).

Biological Surveys:  The results of steelhead spawning surveys for Whiskey Creek for 1993 through 2000 were included in the proposal.  Juvenile densities on McCoy Creek for 1997-2000 were also included.  Both surveys were again conducted in May and July 2001, but have not yet been summarized or reported.  We generally do this in the fall/winter months.  All data will be included in quarterly and annual reports to BPA.  Several miles of McCoy and Meadow creeks were also surveyed for steelhead redds in 2000 (see Appendix 1, Table 4), and a redd visibility study was completed.  We intend to continue with annual surveys of both existing and new study sites.

Additional Monitoring: Beyond the standard monitoring mentioned above, additional monitoring submitted in the 2000 Annual Report to BPA includes 1) monitoring of stream flows on the McCoy Creek/Tipperman channel relocation project to determine the percentage of flow entering the old versus new channels, 2) stability assessments of instream structures (LW) in Meadow Creek, 3) snorkel counts to determine if culverts acted as fish barriers on Milk Creek, 4) installation of bank and streambed pins to monitor erosion in McCoy, Meadow and Catherine creeks, 5) pre-project inventories of streambank stability, overhanging vegetation, and undercut banks using EPA protocol (Appendix 1, Table 6),  6) a pre-project survey of large wood on Meadow Creek indicated a lack of complex pools prior to implementation, 7) Rosgen Level II surveys on Milk and Ladd creeks, 8) longitudinal profile and analysis of fish passage barriers and head cuts on Bear Creek.  Items 6-8 are discussed in the Field Inventories section of the 2000 Annual Report (Appendix 1).

Quarterly reports to BPA for 2001 are not yet complete.  The standard monitoring listed above was repeated in 2001.  Additional M&E and related work that was also conducted to date includes:

- Collected and analyzed past fish monitoring data on Milk Creek (ODFW Aquatic Inventory) and conducted electroshocking surveys in an 850 ft. reach that clearly indicated an old culvert acted as a barrier to juvenile chinook.

- Collected past fish monitoring data on Rock Creek.

- Collected flow data on Ladd Creek (to aid in new channel designs and determine fish passage concerns).

- Field survey of East Fork of Bear Creek (to determine fish presence, flows).

- Completed GIS mapping of all project locations (slide #3 of presentation).

- The project biologist completed a GPS Total Station survey and topographic mapping of the Longley Meadows project, including longitudinal profiles of Bear and Jordan creeks and the Grande Ronde River.

- Contracted aerial photo flights of McCoy, Meadow, Milk and Sheep creeks and the Longley Meadows project (slide #’s 17 & 23 of the presentation) that may be used in both project planning and monitoring.

- Conducted snorkel surveys on the Grande Ronde River.

- Resurvey toe pins installed in 2000 at the confluence of McCoy and Meadow Creek to monitor channel aggradation/degradation (no changes detected).

- Completed Rosgen Level II and III assessments: pebble counts, bar samples, cross-sections, bank and toe pins, longitudinal profile of the old and new Milk Creek channels, particle entrainment calculations and bank erosion hazard index.  Monitored survival of plantings (>70% on willows).

Please note that much of the work listed as “Additional Monitoring for 2002 and beyond” in the project proposal we have already initiated.  Many of these activities are conducted on new projects, particularly where we have used an active restoration approach.  We believe we cannot do active restoration projects without collecting this type of baseline data, and then continue to monitor to assess the effectiveness of projects over time.  We want to insure we will have continued funding to repeat what amounts to a very large increase in our workload, thus we have increased our budget accordingly.

The program has clearly accomplished many habitat and stream restoration activities. Photographs of restoration results illustrated that, with respect to approach and technique, much, perhaps most, of this project’s restoration work is of the passive sort that the ISRP has recommended—removing human abuses and enabling the natural system to restore normative functions. The ISRP recommendations in FY00 called for M&E, and the FY02 proposal responds with am M&E plan but does not present M&E results, leaving the reviewers to question whether M&E was done in FY00-01. Results should be summarized quantitatively in tables and graphs in the FY02 proposal’s project history.

Response:  Please see responses above for details of the M&E done in 2000-01.  We feel that the analysis of passive restoration is easily demonstrated by cost effective, but qualitative photo documentation.  In addition, the information on the habitat transects and stream temperatures monitoring will provide additional details to analyze what changes have occurred.  We provided additional references in the proposal to past or ongoing studies to further substantiate this approach.  Some monitoring and evaluation results were included in the proposal (pgs 16-20, 22-25) in the project history section, and additional details are provided in the first response.  We believe that active restoration approaches do require more rigorous monitoring and evaluation and note in the comments and references above that we have taken the steps to do so.  Obviously we did a poor job of illustrating that we have already moved ahead in our monitoring program.  An example some of this type of monitoring is attached for the ISRP’s review (Milk Creek Channel M&E.xls) in which pre-project data were collected and analyzed to design the new channel, and post-project data were collected to monitor changes in the new channel.

This is a long-standing project that is not providing a quantitative summary of biological or physical results. Data collection and analysis have been a minor component of this project and continue to lack the emphasis they warrant.  However, projects that have been funded since 1984 owe it to the region to provide rigorous internal evaluation of the efficacy of actions in order to understand if the assumptions driving the actions are correct.  After so many years and so many projects (BPA funded and otherwise), it is critical that this project demonstrate physical and biological changes.  It is time to provide an evaluation of the habitat restoration work.

During the presentation the PI’s response to the need for and role of monitoring was candid but disturbing.  He noted that monitoring was cumbersome and done primarily to appease the ISRP for the purpose of continuing funding.  This reflects a serious misunderstanding of the role of monitoring, which is the primary tool for adaptive management – learning and providing course corrections to an ongoing program.  The PI noted that he was certain that they were doing good things for streams and habitat – he and the landowners could see the results with their own eyes – therefore, it wasn’t necessary or even desirable to collect “reams of data” to verify this.  Many of the biologists in the basin appear to have an unvalidated belief in the Rosgen method as the vehicle for achieving the desired stream conditions in the subbasin.  This may prove to be warranted, but it should be critically examined.

The history of fisheries management is replete with well-intentioned, but scientifically unsound practices that people thought were good things to do (e.g., rip-rapping stream banks for stability, channelizing streams for flood protection, eradicating bull trout, widespread outplanting of fry in the early years of the hatchery programs and the wholesale transfer of lower Columbia River chinook into the upper Columbia River).

Response:  Statements of Work and Budgets dating back to the early 1990’s routinely included statements such as “These (M&E) tasks will be accomplished only if adequate time and funds are provided by BPA.”   Additional correspondence over the years with BPA contracting officers clearly indicated that monitoring and evaluation were a distant third in priority behind O&M and Implementation.

In the Response Review of the Fiscal Year 2000 Proposals (ISRP 99-4, 1999) on page 255 the ISRP stated “The primary weakness is the monitoring and evaluation component of the project, which should be improved in future proposals.”   To address this primary concern, in the FY 2002 proposal we 1) summarized the results of our past M&E, 2) strengthened the monitoring on new projects to insure we meet our 7 objectives, and 3) updated the Adaptive Management Implications section.

We have already taken the necessary steps to update our monitoring program and have asked for additional funding to continue to do so.  If the project biologist left the impression during the presentation that monitoring was not important it was certainly unintentional.  The details provided in annuals reports and summarized in Response #1 supports our ongoing commitment to monitoring and evaluation.

The “Adaptive Management Implications”  (pg. 26-28) and the “Additional Monitoring for 2002 and beyond” (25-26) sections of the proposal show some analysis of past M&E, and evaluating its shortcomings.  The “reams of data” comment stem from two thoughts: 1) a frustrated biologist who was reminded of the four 4-inch notebooks of raw, unpublished habitat transect data sitting on shelves in the office, that are a constant reminder that we could be doing more M&E, but time and dollars are allocated to the project priority of O&M or new project implementation, and 2) landowners generally do not need this type of evidence to determine their projects as successful.

It was at the direction of the BPA contracting officers that project biologists attend Rosgen training if we will be conducting instream work activities.  Monitoring and evaluation is a basic tenant of what is taught in Rosgen courses.  In fact, Level IV of the Rosgen hierarchy of river inventory and assessment is the “Validation Level”, whereby various field data measurements of sediment, stream flows, and stability and erosion rates are conducted (Rosgen, 1996, pg.7-1).  We have included this type of data collection in the “Additional Monitoring for 2002 and beyond” section of the proposal, and have already set up monitoring stations on Milk Creek where we used a Rosgen Priority 1 approach, and on Meadow Creek (reported in the 1999 Annual Report to BPA) where a non-Rosgen approach (LW placements) was used.  We will continue to monitor both of these sites, which will provide the opportunity for a quantitative comparison of a Rosgen and non-Rosgen restoration project.

This looks like a good program that has made significant contributions to stream habitat improvements. Such programs are very important, and longer-lived ones like this one can succeed in bringing in many local landowners as cooperators. It is important that this work continue.  Nevertheless, the program has reached a point where it is mandatory that it be critically evaluated.  The PI does not appear to understand the role of and need for M & E, and its role as a guiding and correcting principle in the FWP.  How much technical support is available to the PI for the M&E work? Part of the written agreements with landowners is that ODFW will continue long-term monitoring of these projects. What will be the extent of this monitoring?

Response:    The project biologist and technician are currently doing all of the project level M&E activities.  Outside technical support includes:

- The ODWF Aquatic Inventories Project:  Methodologies and expertise to compare pre-project and post-project habitat conditions on individual projects and identify limiting factors.

- The Research & Evaluate Restoration of Northeast Oregon Streams project No. 200005100 by OSU (in progress): Compares treated and untreated reaches.

- Research work on cold water seeps in the basin by Ebersole, OSU:  Maps of individual sites have been provided to us on several projects.

- The ODFW Spring Chinook Early Life History Project: Identify preferred or limiting habitat or habitat types.

- The Pacific Northwest Research Station:  Monitored chinook and steelhead smolt outmigrants in McCoy and Meadow creeks.

- ODFW district staff:  Collect index and supplemental spawning counts (some of these are within individual project areas) and other critical data.

- ODEQ Biomonitoring Section: Collected fish, macro invertebrates and temperature data in the basin in treated and untreated reaches.

- Oregon Plan Reporting Forms are completed on all individual projects and included in the statewide database.

The last bullet in bold print on slide no. 25 of the presentation regarding our written commitment to landowners was intended to emphasize the importance of O&M (such as fence maintenance), which is generally much more important to landowners than M&E.  It was a reminder that if ODFW/BPA does not live up to our end of the deal then landowners will lose faith in us and we will not have any restoration projects to monitor or evaluate.  With regard to M&E, all projects have as a bare minimum several photopoints established and repeated as a monitoring tool.  The attached project database in Excel includes lists of monitoring done on individual projects.  Photopoints, along with any other monitoring completed such as spawning surveys or temperature data are routinely distributed to interested landowners and agencies.

As we near the end of lease terms, we begin renegotiations with landowners.  One of our goals is to continue with both O&M and M&E on these projects, but it is entirely up to the landowner.  Of the four leases that have expired so far, all 4 landowners have been willing to us to continue O&M or have been doing the work themselves, and all 4 have allow at least some level of continued monitoring.

If the project is to be funded, it is critical that outside assistance be made available to the PI (either through ODFW or perhaps through OSU) to compile, review, analyze, and publish the results of program in stream habitat restoration. An individual with strong quantitative skills should be dedicated fulltime to analysis of the past 15 years’ monitoring data. The results of this analysis should be clearly and comprehensively presented in the next proposal.

Response:  We agree that a more thorough, and preferably independent evaluation of the program is worthwhile.  Unfortunately, according to Oregon State law we cannot make requests for new funds, or increase existing program funds without legislative approval.  Therefore, we propose that we reallocate personnel funds in the proposed 2002 budget by shifting funds that would normally be dedicated to administrative activities such as program supervision and clerical assistance.  This would allow us to contract out a program review to one individual for an estimated 3-6 months.  But it should also be noted that this would also result in less time dedicated to new project implementation.

We are in the process of contacting potential individuals willing to take on the task to compile, review, analyze and publish the results of our habitat restoration efforts.  Contacts have been initiated with OSU and the ODFW Aquatic Inventory Project.  If we can conduct this within the 2002 budget as proposed, we should be able to initiate a contract beginning in March, which is the start of the 2002 budget cycle.

APPENDIX 1- excerpts from 2000 Annual Report to BPA

(Entire report is attached separately as a pdf document)

(From pg. 16 in annual report)

##### Field Inventories

Several project areas were inspected to assess pre-project conditions (identify limiting factors), or to determine success/failure of previous implementation activities:

A pre-project survey of large wood (>12 inch dia. x 35 ft. long) was conducted on the Meadow Creek/Habberstad project.  Only 9 pieces of LW were found within the bankfull area in the 1.1- mile reach, and 5 of these were old bridge members.  High summer water temperatures and lack of large pools (which are often created by large wood) are key limiting factors that will be addressed in this project.  Streambank stability, overhanging vegetation and undercut banks were also monitored on this project before implementation.  Only 66.5% of the banks were classified as covered and stable (Table 6).  We expect that by excluding livestock along with other improvements in management that over time the percentage of stable banks will increase.

A Rosgen level II stream analysis (longitudinal profile, 6 cross sections, pebble counts) was completed on 630 ft. of Milk Creek to help in planning the construction of 1,300 feet of new channel in the area immediately downstream.

A Rosgen Level II stream survey was completed on a 1,436 ft. reach of Ladd Creek.  The information will be used to help plan the relocation/conversion of 1.7 miles of existing irrigation ditch into approximately 2.2 miles of natural stream channel.

Log weirs previously installed by NRCS and the GRMWP on the Bear Creek/Alta Cunha Ranches property were reviewed to assess fish passage problems during low summer flow.  ODFW requirements for a 6-inch maximum jump height for juveniles were not being met on any of the 21 weirs, none of these had jump pools on the downstream sides to facilitate jumping, and most of the weirs were completely de-watered by late June (Figure 12).  A longitudinal profile from the highway to the mouth (0.5 miles total) was taken to help identify other headcut areas below the weirs that were also inhibiting fish passage.  ODFW and the CTUIR conducted repair work in October.

(From pgs. 29-39 in annual report)

MONITORING AND EVALUATION:

##### Photopoint Establishment

Eleven new photopoints were established on the Meadow Creek/Habberstad project and 7 established on the Milk Creek/Hall Ranch project.  Photopoint descriptions were written for these new projects.  Prework and post-work photopoints were taken of all instream work sites on Meadow, Bear, Milk and Camas creeks, using the digital camera.

##### Photopoint Picture Taking

Two hundred twenty nine photopoints of a total of 261 were retaken in 2000.  All photopoint pictures were processed, labeled, and filed in permanent notebooks.  Before/After photopoint pictures of Beaver, Chesnimnus, Pine, Salmon and Whiskey Creek were scanned or reproduced and given to their respective landowners, or included in quarterly and annual reports.

##### Habitat Monitoring Transect Establishment and Data Summarization

In the Upper Grande Ronde drainage 40 habitat monitoring transects were established on Sheep Creek and 40 on McCoy Creek in 1988. In the Joseph Creek drainage 30 transects were established on Elk Creek and 30 on Chesnimnus Creek in 1988.  All data sets from the original measurements were entered into a summarization program on Dbase III Plus in 1993, but data has yet to be summarized.  Habitat Monitoring data collection was repeated on 40 transects on McCoy Creek and 40 transects on Sheep Creek in 2000.

##### Thermograph Data Collection and Summarization

Hourly temperature data have been recorded, collected, summarized and graphed from thermographs in Sheep and McCoy creeks since 1988; from Salmon Creek since 1991; Beaver and Camas creeks beginning in 1994; and Meadow Creek starting in 2000.  New lock boxes were constructed for all thermographs.  New Starlogger thermographs were set up and installed on Sheep, Salmon and McCoy creeks.  These replaced the Ryan Tempmentors, which have performed poorly in the past.  Instructions for deployment and summarization were updated in Excel format.  All 12 thermographs were checked in July and all but one (upper Beaver Creek) were functioning normally.

##### Thermograph Data Analysis

It is important to keep in mind tolerances of salmonids to changes in water temperatures as we analyze the data. The upper lethal limit for chinook salmon has been reported as 26.2oC, and the lower lethal limit at 0.8oC.   Upper and lower lethal limits for steelhead are 23.9oC and 0.0oC (Meehan, 1991).  The Independent Scientific Group (ISG, 1996) also reviewed available information and concluded that the thermal requirements for chinook salmon are approximately as follows:

|  | TEMPERATURE |
| --- | --- |
| LIFE STAGE | Optimum | Range | Stressful | Lethal* |
| Adult migration and spawning | 50 oF (10 oC) | 46.4 -55.4 oF (8 –13 oC) | >60 oF (>15.6 oC) | >70 oF (>21 oC ) |
| Incubation | <50 oF (<10 oC) | 46.4 -53.6 oF (8-12 oC) | >56 oF (>13.3 oC) | >60 oF (>15.6 oC) |
| Juvenile rearing | 59 oF (15 oC) | 53.6-62.6 oF (12-17 oC) | >65 oF (>18.3 oC) | >77 oF (>25 oC) |

*  Lethal is for 1-week exposures, higher temperatures may be tolerated for shorter exposure times.

The ISG also concluded that other salmonid species are not markedly different.  Salmonid populations are able to respond to temperature changes by moving upstream or downstream to find thermal refuges.  Warming of streams, however, may concentrate salmonids into small areas where they may be more susceptible to predation (see 1998 Annual, Appx 3), or lead to invasion of non-native species (Ebersole and others, 1994).  In 1996 the Oregon Department of Environmental Quality (ODEQ), in accordance with an Environmental Protection Agency mandate, listed water quality limited streams in the state.   The “303(d)” list included guidelines for stream temperatures; streams whose 7-day average of the daily maximum temperatures exceeded 17.8o Celsius (64o Fahrenheit) were listed as being thermally polluted, and are considered to have sub-lethal temperatures for salmonids and other cold-water species.

# Analysis of summer stream temperature data by site are summarized below:

Salmon Creek:

Thermographs were installed at two sites in 1991.  The upper site is located at the upstream end of the McDaniel property at RM 2.4.  The lower site is near the mouth at RM 0.1, on the McClaran property.  Riparian fencing at the upper site was completed in 1990; the lower site was fenced in 1989.

Salmon Creek has consistently shown cooling of stream temperatures as water travels downstream through the riparian corridor.  In 1992, comparison of upper and lower summer mean weekly maximum temperatures showed an average cooling of 1.69oC at the lower (downstream) thermograph.  In the summer of 2000 the average was 3.77oC cooler at the lower end (Figure 14).  Temperature fluctuations averaged 6.7 oC at the lower site compared to 11.2 oC at the upper site, indicating cooler, stable, and more favorable conditions in the lower reaches.  Salmon Creek is a small mid-elevation stream, and despite some recent heavy flooding, the vegetation is now in better condition to prevent damage from high flows, and there has been a considerable increase in the amount of shade along this reach.  The stream channel has narrowed and deepened, reducing the stream water surface area and amount of solar radiation reaching the creek.  There are also inputs of ground water from some springs that were also fenced off in 1990 which are also becoming more shaded.

Figure 14.  Mean weekly summer temperature data on Salmon Creek in 2000, at RM 2.4 (Upper) and RM 0.1 (Lower).

McCoy Creek:

Two thermographs were installed in 1988 on the Misener/Tipperman property; riparian fencing was constructed in the same year.  The lower site is located near the mouth of McCoy Creek, and the upper site is about 1.6 miles upstream, at the head of a canyon.  In 1997 the McCoy Meadows channel relocation project was implemented in the upper meadow (RM 0.8 to RM 1.5), which diverted the channel into one of the pre-1970 channels.

In 1988, the first year of data collection, summer mean weekly maximum temperatures at the lower (downstream) site averaged 3.70oC warmer than the upper site.  In 2000 the average was 2.05 oC warmer (Figure 15).  Temperatures at the lower site continue to be very warm and show large daily fluctuations, but data collected during the 13-year period suggests a cooling trend may now be developing.   It is too early to tell if the pattern will continue.

Figure 15.   Summer temperature data on McCoy Creek in 2000, at RM 1.6 (Upper) and RM 0.0 (Lower).

Sheep Creek:

Thermographs were installed in 1988 on the Vey property and fencing was completed the same year.  The upper site is located at RM 6.7 near the U.S. Forest property boundary.  The lower site is located 4.3 miles downstream at RM 2.4 and about 100 feet upstream from the bridge along F.S. Road 51.

Comparison of summer mean weekly maximum temperatures shows that lower Sheep Creek averaged 1.46oC warmer than the upper site in 1988 and 0.82 oC warmer in 2000 (Figure 16).  Data for the month of October, however, has not yet been included.  Data collected over the 13-year period continues to show moderate and consistent warming of 1 to 3oC at the lower thermograph, with no apparent trends developing to date.  Daily fluctuations at both sights are moderate compared to other sites.

Figure 16.  Summer temperatures on Sheep Creek in 2000 at RM 6.7 (Upper) and RM 2.4 (Lower).

Beaver Creek:

ODFW installed Hobo Temp thermographs at the mouth of Beaver Creek, and at the Crown-Pacific/ U.S. Forest Service property boundary at RM 5.9 in July 1994.  These were replaced in November 1994 with Unidata Starlogger thermographs that also recorded ambient air temperature.  Riparian fencing was completed on the lower half of the study area in 1993, and on the upper half in 1994.

Comparison of Beaver Creek mean weekly maximum water temperatures in 2000 showed continued warming of water moving downstream as has been observed in past years (Figure 17).  The thermistor at the upper site was out of the water for three weeks so data could not be compared to past years.  Stream temperatures at the Upper Beaver Creek site, however, are one of the few places we have monitored that generally stay within the ODEQ water quality standards 17.8oC.  The standard was only exceeded in 5 weeks of the 26 week period, in what was a warmer than average summer.  A large portion of the upper drainage is within the protected La Grande City Watershed.

Figure 17.   Summer temperature data on Beaver Creek in 2000, at RM 5.9 (Upper) and RM 0.0 (Lower).

Camas Creek:

Permanent Unidata Starlogger thermographs were placed at the upper and lower ends of the project area in May of 1995, recording stream and ambient air temperatures.  Riparian corridor fencing was completed in 1995.  The upper site is located about 0.3 miles downstream of Lehman Hot Springs Road at RM 29.6; the lower site is about 2.8 miles downstream at RM 26.8 at the Pendleton Ranches/Forest Service property boundary.  Comparison of summer mean weekly maximum temperatures showed that the lower Camas Creek site in 2000 averaged 2.03oC warmer than the upper (Figure 18).   However, the data for the month of October has not yet been entered.  In 1998 and 1999 temperatures at the lower site averaged slightly cooler (0.10oC and 0.45oC respectively) than the upper site, indicating that no consistent pattern of either cooling or warming has developed.

Figure 18.  Summer temperature data on Camas Creek in 2000, at RM 29.6 (Upper) and

RM 26.8 (Lower).

Meadow Creek

Permanent Unidata Starlogger thermographs were installed at the upper and lower ends of the Alta Cunha Ranches projects at river miles 10.3 and 8.7 in May of 1999. Both units were set up to record water and ambient air temperatures. This was the first year of complete data collection, and indicated slightly (0.20 oC) cooler water at the downstream end of the project (Figure 19).

Figure 19. .  Summer temperature data on Meadow Creek in 2000, at RM 10.3 (Upper) and

RM 8.7 (Lower).

##### Miscellaneous Monitoring & Evaluation Activities

ODFW personnel repeated steelhead spawning surveys on Whiskey and Little Whiskey creeks in April and May 2000.  Four live fish and 16 redds were found.  The redd counts were the highest observed since counts began in 1993 (Figure 19).  McCoy and Meadow creeks were also surveyed (Table 4).  In addition to surveying the Index reaches, several miles of non-index streams were checked this year that had not been done in many years.  Streams were surveyed 4 separate times at approximately 2 week intervals to identify peak spawning times and determine how long a redd remains visible after initial spawning.   Redds sizes, locations in the channel, water depths and visibility were measured during each survey.   The results are summarized below.

| TABLE 4. Summary of Repeat Steelhead Spawning Surveys in Upper Grande Ronde Basin Streams, 2000. |
| --- |
| STREAM | REACH | Location (River Miles) | No. Redds | Miles Surveyed | Redds/mile | Live Fish |
| McCoy Cr | F.S to Cunha (index plus) | 7.0-10.0 | 0 | 3.0 | 0.0 | 0 |
| McCoy Cr | Cunha to Snow | 3.0-7.0 | 7 | 4.0 | 1.8 | 0 |
| McCoy Cr | Snow to upper Tipperman | 2.0-3.0 | 1 | 1.0 | 1.0 | 0 |
| McCoy Cr | Upper Tipperman to Mouth | 0.0-2.0 | 6 | 2.0 | 3.0 | 1 |
| Meadow Cr | F.S. index to Cunha | 10.3-17.5 | 4 | 7.2 | 0.6 | 3 |
| Meadow Cr | Cunha to Taylor | 7.0-10.3 | 1 | 3.3 | 0.3 | 0 |
| Meadow Cr | Taylor to Dark Canyon | 1.5-7.0 | 1 | 5.5 | 0.2 | 0 |
| Little Whiskey Cr | Upper Courtney to mouth | 0.0-1.0 | 3 | 1.0 | 3.0 | 0 |
| Whiskey | Upper Courtney to mouth | 0.0-3.6 | 13 | 3.6 | 3.6 | 4 |
|  |  | TOTALS: | 36 | 30.6 | 1.2 | 8 |

Spawning was generally completed by mid-May, and redd visibility deteriorated rapidly after two weeks.  Overall, redd counts in these streams were low at 1.2 redds/mile, and were particularly low in the index survey areas.  However, in the McCoy Creek- Upper Tipperman to Mouth reach we found 6 redds where none had been observed in many years.

Figure 19.  Redd counts on Whiskey Creek and Little Whiskey Creek, 1993-2000.

A spring chinook spawning survey was conducted on 6.2 miles of Sheep Creek on September 7, 2000.  No redds or adult fish were observed.  It was noted during the survey that juvenile Rb/St were abundant, and several juvenile chinook were observed.

The technician assisted ODFW John Day district personnel with spring chinook spawning counts on Camas Creek.  Six live fish were observed downstream of the project area, but no redds or fish were found in the Pendleton Ranches project reach.

Stream flows in McCoy Creek in the old and restored channels were calculated at 402 cfs on March 29th, and showed that 75% of the flow is now going into the restored channel and 25% into the abandoned channel.  Additional electroshocking was conducted in the abandoned channel to determine the extent of stranding that occurred during receding flows, and because instream work activities were conducted in this section this summer.  A total of 27 age-0 and 10 age-1 steelhead were removed and transported into the restored channel.

Instream wood placed in 1999 on the Meadow Creek/Alta Cunha ranches project was monitored for stability during near-bankfull flow (370 cfs) events.  Over 70% of the key structures showed no significant movement following an above average flow year.  Of the 30% that did move, most of the shifting was minor, for example, a tree tip swinging from across the stream channel to parallel to the channel.  Structures were also checked to determine if the larger key pieces were effective at trapping smaller wood.  Over 60% of the structures trapped additional wood, up to 40 individual pieces in one case.  Site schematics and an inventory of the number of pieces of wood and individual sizes were completed on the Meadow Creek/Habberstad instream project.  These sites will be monitored in a similar manner in 2001.

Electroshocking surveys were repeated in McCoy Creek on June 30, 2000 (Table 5).  One of the four stations was not sampled in 2000 due to low water conditions in the former channel.  Juvenile Rb/St densities were 0.11 fish/m2 in 2000, up somewhat from the 1999 counts.  Overall abundance of other fish species was also higher than the last 2 years, but remained below the 1997 counts (Figure 20).

| TABLE 5. Fish Population Estimates in three 50 meter ODFW Monitoring Stations of McCoy Creek, June 30, 2000. |
| --- |
|  | SAMPLE SECTION | COMBINED TOTALS |
|  | FS-1 | FS-2 | F-1 | Total Number | DENSITY | SPECIES |
| SPECIES | (RM 0.7) | (RM 0.2) | (RM 1.4) | Of Fish | FISH/m^2 | COMP. |
| Rb/St | 33 | 23 | 22 | 78 | 0.11 | 5.6% |
| Sculpin | 97 | 9 | 14 | 120 | 0.17 | 8.7% |
| Dace | 118 | 344 | 75 | 537 | 0.77 | 38.8% |
| Shiner | 91 | 153 | 250 | 494 | 0.71 | 35.7% |
| Sucker | 13 | 120 | 5 | 138 | 0.20 | 10.0% |
| Pikeminnow | 5 | 5 | 3 | 13 | 0.02 | 1.0% |
| Bullhead | 0 | 0 | 0 | 0 | 0.00 | 0.0% |
| Chiselmouth | 1 | 1 | 0 | 2 | 0.00 | 0.1% |
| Totals: | 358 | 655 | 369 | 1,382 | 1.99 | 100.0% |

Figure 20.  Fish population estimates and densities (fish/m2) of Rb/St and other fishes in McCoy Creek, 1997-2000.

Snorkel counts of fish in Milk Creek were conducted to determine general fish composition and distribution prior to project implementation.  Very few fish were observed above the existing highway culvert, which appears to be acting as a barrier to juvenile fish movement during summer flows.  Sample sites were also set up on Beaver, Meadow, and Sheep creeks.  Snorkel counts were conducted to monitor fish species general composition and abundance.

The technician inspected an eroding bank on Catherine Creek where a landowner complained of excessive flood damage.  No work is necessary at this time, but rebar pins were installed to monitor streambank and bed erosion.  The erosion pins will help us determine if bank protection will be necessary.  Three toe pins were installed and surveyed in at the confluence of McCoy and Meadow creeks to monitor changes in channel bed elevation.

Pre-project surveys of streambank stability, overhanging vegetation and undercut banks using EPA (1993) protocol were conducted on 4.05 miles of the McCoy Creek/Alta Cunha Ranches project, and on 1.1 miles of the Meadow Creek/Habberstad project.  The results are summarized below:

| TABLE 6. Pre-Project Inventories of Streambank Stability, Undercut Banks and Overhanging Vegetation on McCoy and Meadow Creeks, 2000. |
| --- |
|  | Percent of Total Stream Length |
| STREAM | Covered & Stable | Covered & Unstable | Uncovered & Stable | Uncovered & Unstable | Undercut Banks | Overhanging Vegetation |
| McCoy Cr. | 59.89% | 20.73% | 6.66% | 12.73% | 1.46% | 0.48% |
| Meadow Cr. | 66.46% | 24.42% | 4.49% | 4.62% | 2.28% | 1.63% |

Both streams appear to be below potential for the given stream and valley types, and we believe 70% or better in the “Covered & Stable” category are attainable under improved management practices.  Even though the McCoy Creek section had been rested from grazing for 2 years there was still a high proportion of unstable banks and a poor shrub component indicated by the low percentage of overhanging vegetation.

Bird boxes were cleaned and inventoried on Camas Creek.  Bluebirds or wrens had utilized twenty-five of the 32 boxes (78%).  Bird boxes were cleaned and inventoried on Meadow and McCoy creeks by the landowner.  Bluebirds utilized 20.2% of the boxes, Tree Swallows 15.2%, House Wrens 30.9%, other birds used 9.4%, and 24.2% were empty.

Attachments:

Annual Report

Database

Milk Creek Spreadsheet