RESPONSE TO ISRP COMMENTS

Project Number: 199801700

Eliminate Gravel Push-up Dams in Lower North Fork John Day

Sponsor: North Fork John Day Watershed Council

Please find below the requested maps detailing the three project

sites for this funding year (2001) and also project sites for the

next two funding years.  Project sites are chosen through a

prioritization process involving the North Fork John Day Watershed

Council, Monument SWCD, Oregon Department of Fish & Wildlife, and the

Confederated Tribes of the Warm Springs John Day Basin Office.

Landowner interest and participation has grown each year of the

project.   Prioritization criteria includes the degree of passage

impediment/restriction, and the amount and severity of annual

disturbance in installation of the push-up dam.  It is anticipated

that prioritized dams in the Monument/Kimberly reach can be

eliminated by the end of the 2004 construction season.  Remaining

temporary push-up dams will be small in scale and will not impede

anadromous or resident fish migration and will result in minimal

annual disturbance.  The North Fork John Day Watershed Council and

Monument SWCD will continue working with landowners to design and

install alternatives to these remaining small, temporary structures.

The included maps provide a picture of the distribution of current

push-up dams as well as those eliminated during the life of this

project.  Significant progress has been made in eliminating the

larger structures with the most adverse impact on passage/migration

and riparian conditions.  Project methods are site-specific and

becoming increasingly more so over the life of the project.

Permanent pumping stations are designed by NRCS and contracted

engineers and all designs and installations  meet NMFS and USF&WS

criteria.  Consultation is completed by the North Fork John Day

Watershed Council coordinator.

Tier 1 monitoring was chosen due to the nature of the project and

to best coordinate with existing monitoring efforts on the North Fork

John Day.  Trend monitoring may eventually provide information and

data illustrating the local effect of annual instream disturbance on

water quality, riparian health, and riverine conditions.  Photopoints

of project sites provide a long-term indication of riparian recovery

and health.  There is currently underway an effort to integrate and

coordinate water quality and biological monitoring efforts in the

John Day Basin.  This will maximize the efficiency of existing

efforts and help target and prioritize future monitoring within the

Monument/Kimberly reach of the North Fork John Day.  The NorthFork John Day Watershed Council has limited staff and resources.  Coordination of existing efforts and integration of data previously compiled and stored is essential to our monitoring program.

TownShip Range  T9S R27E

Monument/Kimberly Reach and 199801700 Project and Proposed Project Sites

Upper Section

Middle Section

T9S R26E

Lower Section