Project 28059

Restoring anadromous fish habitat in the Lapwai Creek watershed

Response to ISRP Preliminary Review

Nez Perce Soil and Water Conservation District

3113 East Main Street

Lewiston, Idaho 83501

208-746-9886 ext 3

October 12, 2001

ISRP Comment No. 1

Prioritization of a thorough watershed assessment is needed before progressing further.

## Response to Comment No. 1

Several studies have been completed within the Lapwai Creek watershed.  These include;

Lapwai Creek Aquatic Assessment.  Draft completed by Nez Perce Tribe August 2001.

Supplement #1 – Watershed Protection Plan – Environmental Assessment.  Mission-Lapwai Creek Watershed.  September 1994.  This study focused on approximately 40% of the watershed acres. *

Supplemental Watershed Protection Plan – Environmental Assessment.  Supplement Number 2.  This study includes the remaining 60% of the watershed acres.*

*Copies of these documents were mailed to the ISRP review panel on 10/12/01.

ISRP Comment No. 2

The extent of BMPs implementation planned and completed, and what percentage of the work this represents, particularly in relation to reductions in negative attributes that will benefit fish.

## Response to Comment No. 1

The following table outlines the extent of BMPs identified as needed for watershed and fisheries habitat protection in the December 2000 Environmental Assessment.  None of the practices listed in this table have been installed to date.

The following are the BMPs and extent identified as needed.  Our goal is to implement 30% of these within 3 years.

Land Treatment Practice	Unit	   Units

Riparian Treatment Practices

Animal Trails and Walkways	LF	1,300

Channel Vegetation	Acre	130

Constructed Wetland	acre	10

Fencing, Riparian	LF	47,700

Fish Stream Improvement	EAch	53

Grade Stabilization Structure	Each	40

Riparian Flood Plain Easement	LF	4,000

Stockwater Development	Each	30

Streambank & Shoreline Protection	LF	20,000

Use Exclusion	Acre	20

Animal Feeding Operation (AFO) Practices

Dike	LF	5,000

Diversion	LF	7,500

Fencing, CAFO	LF	8,000

Stockwater Development	EACH	20

Waste Management System	EACH	7

Road Practices

Access Road (Spot Road Rocking)	LF	100

Critical Area Planting	Acre	25

Grade Stabilization Structure	Each	68

Waterway (rock lined)	LF	2,720

Runoff Mgt. System	Each	50

Cropland Practices

Buffer Strip	Acre	25

Diversion	LF	15,680

Filter Strip	Acre	25

Grade Stabilization Structure	Each	82

Grassed Waterway	Acre	33

Nutrient Management	Acre	30,000

Pasture/Hayland Planting	Acre	50

Pesticide Disposal System	Each	50

Pest Management	Acre	30,000

Reservoir Tillage	Acre	1,000

Residue Mgt, No-till	Acre	15,000

Sediment Basin	Each	100

Slot Tillage	Acre	1,000

Soil Testing	Each	150

Stripcropping, Field / Divided Slopes	Acre	1,000

Subsoiling	Acre	5,000

Terrace	LF	17,360

Water & Sediment Control Basin	Each	170

Water Well Testing	Each                  50

Forestland Practices

Critical Area Planting	Acre	 150

Fencing	LF	40,000

Forest Site Preparation	Acre	1,000

Forest Stand Improvement	Acre	2,000

Pasture and Hayland Planting	Acre	3,000

Stockwater Development	Each	30

Tree Establishment	Acre	50

#### Range/Pasture Practices

Fencing	LF	12,000

Heavy Use Area Protection	Acre	10

Pest Management	Acre	5,000

Ponds	Each	10

Prescribed Grazing	Acre	12,000

Range Planting	Acre	3,000

Stockwater Development	Each	20

Use Exclusion	Each	15

Wildlife Practices

Wildlife Upland Habitat Management	Acre	20

Wildlife Wetland Habitat Management	Acre	20

The NPSWCD completed six conservation plans in September 2001.  These plans include the designs and site specific BMPs identified above.  If funded by BPA, these projects will be ready to implement in 2002.

The proposed BMP treatment measures will reduce the water temperatures of Lapwai Creek and tributaries and off-site sediment and associated nutrient loading will be reduced by 46 percent (2000 NRCS Environmental Assessment).  The planned temperature and sediment reductions will have a positive effect on both the resident and anadromous fisheries present in the watershed.

The establishment of adequate multi-layered riparian vegetation on 53.0 miles of stream length will enhance the fisheries habitat by not only achieving much needed temperature reductions, but also allowing for the re-introduction of large organic debris into the stream system.

No adverse impact will occur to the candidate plant species under the ESA since all earthmoving/ground-disturbing activities associated with structural implementation will occur on cropland.

The BMP measures will not cause any short-term or long-term adverse impacts to anadromous and resident fisheries or other aquatic resources.  Enduring practices proposed for installation are in areas where active erosion is currently taking place.  Conservation objectives are to stop sediment entering the creek and reduce excessive water temperatures throughout the summer.  No additional sediment will be delivered to Lapwai Creek or the Clearwater River during the installation of the project.  The long-term benefit of this project will be a seasonal temperature reduction coupled with a reduction of sediment delivered to the spawning and rearing areas in Lapwai Creek and the Clearwater River.

Installation of enduring practices in the upper watershed is expected to modify present hydrologic conditions of the watershed to better simulate presettlement conditions by reducing the present peak flows.  This may allow for increased late summer flows as water, which is retained even for short periods by the enduring practices, which may be available for later-season baseflow, either as soil moisture or deep percolation.

No adverse effect on the Snake River fall and spring/summer salmon and its' designated habitat are expected.  With the reduction of sediment delivered to Lapwai Creek, impacts should be positive to all aquatic resources downstream.

Effects on Resources of Principal National Recognition

Principal Sources of	Measurement

Types of Resources	National Recognition	of Effects

Air Quality	Clean Air Act, as amended	No effect

(42 U.S.C.7401 et seq.)

Endangered and threatened	Endangered Species Act	Bald eagle, no adverse

critical habitat	of 1973 as amended	effects. Snake River fall

(16 U.S.C.1531 et seq.)	and spring/summer

chinook  salmon and

West Coast steel head,

not likely to adversely

effect.

Fish and wildlife habitat	Fish and Wildlife	Positive effect on the

Coordination Act   	anadromous fishery.

(16 U.S.C.Sec.661 et seq.)

Floodplains	Executive Order 11988,	Positive effect due to

Floodplain Management	riparian enhancement

and decreased

sedimentation

### ISRP Comment No. 3

Indicate how the project will be monitored and evaluated, and the level of monitoring.

# Response to Comment No. 3

Objectives 8 and 9 in the proposal address M&E issues.  Objective 8 tasks include the collection of site specific BMP monitoring to evaluate the effectiveness of the installed BMP in reducing sediment and nutrients delivered to the stream and /or reducing the stream temperature, or improving the in-stream habitat.  This type of monitoring is a Tier 1 – (trend or routine monitoring).

Objective 9 tasks include the continued monitoring of stream temperature within the Lapwai Creek watershed.  This project is part of an on-going effort with the Nez Perce Tribe, Natural Resources Conservation Service, Idaho Soil Conservation Commission, Idaho Fish and Game and the Idaho Association of Soil Conservation Districts.  This type of monitoring is considered a Tier 1 (trend or routine monitoring).  The results from this monitoring will be published in a regional stream temperature report for use by all interested parties.

In addition, fish population data will be collected by the Nez Perce Tribe (NPT) and Idaho Fish and Game (IDFG) as outlined in BPA proposal number 199901700.  The NPSWCD will assist with this project by coordinating landowner access and supplying labor for field crews.  However, the data analysis will be completed by the NPT and IDFG.

### ISRP Comment No. 4

Clearer statement of priorities and a list of tasks by order of importance and timing of implementation.

# Response to Comment No. 4

A task list by timing of implementation is listed below.  Items highlighted are high priorities.

Time Frame	Priority	Task

2002-May	1	Collect planning information to prioritize BMP installation

to August		Tasks include completing the stream visual assessment

protocol along 40 miles of stream, complete a GIS road

layer, completion of a GIS noxious weed layer.

2002-August	2	Obtain participation from eligible landowners.  Tasks

to November		include obtaining landowner names/addresses,

developing a GIS coverage of identified landowners,

conducting public informational meeting, developing

outreach materials.

2002-November	3	Complete BMP plans and designs.

to May 2003		Tasks include ranking project applications, site visits,

developing contracts with landowners.

2003-March 	4	Implement BMPs.

to Sept 2005		Tasks include completing NEPA requirements, local

permits, obtaining bids, staking projects, construction

inspection, and final construction approval.

2003-March 	5	Coordinate with other agencies.

to Sept 2005		Tasks include sharing monitoring results, project

priorities, and application results.

2003-March 	6	Complete monitoring and evaluation activities.

to Sept 2005			Tasks include monitoring installed practices, stream

temperature monitoring, and a multi-layer riparian

assessment.