APPENDIX 2: WATER CHARACTERISTICS THAT SHOULD BE EVALUATED PRIOR TO SITING SALMON RECOVERY PROJECTS

| Characteristic | Standard | Source of Standard |
| --- | --- | --- |
| Aluminum | < 0.01 mg/L Not >0.005 mg/L when pH < 6.5 and Ca2+ < 4.0 mg/L Not >0.1 mg/L when pH > 6.5 and Ca2+ > 4.0 mg/L | WDFW Alderdice1 Alderdice1 |
| Ammonia (un-ionized) | < 0.0125 mg/L | WDFW |
| Arsenic | < 0.05 mg/L | WDFW Bell |
| Barium | < 5.0 mg/L | WDFW Bell |
| Cadmium | Not > 0.0002 mg/L 0.001 mg/L < 0.0005 mg/L when alkalinity > 100 mg/L < 0.005 mg/L when alkalinity < 100 mg/L | Alderdice1 Bell WDFW WDFW |
| Calcium | Not < 10.0 mg/L for eggs | Alderdice1 |
| Carbon Dioxide | < 1.0 mg/L | WDFW |
| Chloride | < 4.0 mg/L | WDFW |
| Chromium | <0.03 mg/L 0.01 mg/L | WDFW Bell |
| Copper | < 0.006 mg/L when alkalinity < 100 mg/L < 0.03 mg/L when alkalinity > 100 mg/L | WDFW |
| Dissolved Oxygen | > 7 mg/L | WDFW |
| Fluoride | < 0.5 mg/L | Bell |
| Hardness | < 20 mg/L as CaCO3 | WDFW |
| Iron | < 0.1 mg/L | Bell |
| Lead | < 0.02 mg/L | Bell |
| Magnesium | < 15 mg/L | WDFW |
| Manganese | < 0.01 mg/L | Bell |
| Mercury | < 0.0002 mg/L 0.05 mg/L | WDFW Bell |
| Nickel | < 0.01 mg/L | WDFW |
| Nitrate (NO3) | < 1.0 mg/L | WDFW |
| NO2 | < 0.1 mg/L | Bell |
| Nitrogen (N2) | <110% Total Gas Pressure (TGP) 100 – 104% TGP no problem | WDFW Alderdice1 |
| Characteristic | Standard | Source Of Standard |
| Nitrogen (N2) continued | 104 –109% Chronic problems, 4 – 5% mortalities >110% TGP Acute problem, complete mortality < 103% Nitrogen gas | Alderdice1 Alderdice1 Bell |
| Petroleum (oil) | <0.001 mg/L | WDFW |
| pH | 6.5 – 8.0 6.5 –6.6 Threshold for eggs | WDFW Alderdice1 |
| Potassium | < 5.0 mg/L | Bell |
| Salinity | < 5.0 parts per thousand | WDFW |
| Selenium | < 0.01 mg/L | WDFW |
| Silver | <0.0003 mg/L | WDFW |
| Sodium | < 75.0 mg/L Not < 1.0 mg/L for eggs | WDFW Alderdice1 |
| Sulfate | < 50.0 mg/L | WDFW |
| Zinc | < 0.005 mg/L | WDFW |

Alderdice and McLean (1982) point out that heavy metal concentrations can be determined in a variety of ways, e.g. via total, dissolved or extractable analyses.  They recommend that dissolved analyses be used since heavy metal toxicity is closely correlated with dissolved metal concentrations.  In this same report they indicate that some water characteristics can increase or decrease the toxicity of metals.  For instance, the resistance of fishes to metals generally increases as hardness (mg/L CaCO3) and pH increase.  Furthermore, some metals can have additive deleterious effects and therefore even though individually their concentrations may be acceptable once combined with other metals they can become harmful.  Finally, exposure duration obviously plays a role in the impact of various water borne components on the well being of fish. In some instances pre-exposure to heavy metals during incubation or early stream life may give fish greater resistance to metals in solution.  On the other hand, prolonged exposure to seemingly low levels may be more harmful than short exposures to higher ones. For these and other considerations the interpretation of water quality information can be complex. Therefore it is recommended that a water quality expert review and comment on the chemical analyses that will be performed during a site determination process.

References:

Alderdice1, D.F. personal communication

Alderdice, D.F. and W.E. McLean. 1982. A review of the potential influence of heavy metals on salmonid fishes in the Campbell River, Vancouver Island, B.C.  Canadian Technical Report of Fisheries and Aquatic Sciences No. 1104. 60 pp.

Bell, M.C. 1984. Fisheries handbook of engineering requirements and biological criteria.  North Pacfic Division, Portland. Fish Passage Development and Evaluation Program. 290pp.

WDFW—internal water quality standards