# MFWP Responses to ISRP Comments on our FY 2007-2009 Project Proposal

### 199500400 – Libby Mitigation Program

Project Title:  Mitigation for the Construction and Operation of Libby Dam

Sponsor: Montana Fish, Wildlife & Parks

Location: Mountain Columbia Province – Kootenai Subbasin

Short Description: Implementation of watershed-based habitat enhancement and fish recovery actions to mitigate the losses caused by hydropower in the Kootenai subbasin. Montana Fish, Wildlife & Parks collaborates with the Tribes of Montana and Idaho, IDFG and B. C., Canada.

ISRP Recommendation: Response requested

ISRP Comments:

This is a reasonably thorough proposal for mitigation via habitat enhancement that nonetheless needs better justification through monitoring results for continuing its “hard” stream restoration approaches. 

The proposal provides generally good background, from general Libby Dam effects to specific project streams. The work is largely related to the Council's Fish and Wildlife Program and Libby Mitigation Plan, although justification might have gone broader. There is a rather good narrative of interrelationships with other projects. The objectives for the proposed work include continued stream restoration, removal of non-native salmonids with toxicants, and burbot stock assessment. Soundness of the techniques depends on the results produced. Results of the enhancement actions presented here do not provide convincing evidence that the methods are generating benefits.

The proposal provides a good history that emphasizes actual results not just tasks undertaken. Results of the recent phase of the Libby Creek lower Cleveland restoration are given in good detail for physical and biological attributes. Results of this one restoration effort were presented and reviewers were asked to seek results of other projects in reference material. Detailed results of the one project were useful, but it would have been helpful had some statements been included to summarize results of other projects.

The previous ISRP reviewers were concerned that stream restoration efforts seemed to be following too much of a "hard-engineering" path. That concern is heightened by the proposal’s reporting of the lower Cleveland results. These results call into question the "hard" fixes/active restoration, but the proposal continues to emphasize heavy equipment, logs, and rocks. The cutthroat trout seem to be responding to the restoration activities as a disturbance and avoiding the area. 

Response is needed to address: a) the extent to which passive rehab has been considered, and why the approach was discounted, and b) reasons why proposed stream work (nearly 1/2 of funding requested is for heavy equipment and structural materials) is expected to produce better results than shown so far. The proposal needs to judge whether the sponsors see the lower Cleveland project as "successful" with reasons why or why not. Monitoring should be enhanced until the present projects show the strategy described is beneficial.

Response to the ISRP comments:

a)  We have considered using passive restoration techniques on many of the projects described within the FY2007-2009 project proposal.  However, most of the sites described are not suitable for passive type restoration techniques due to the extremely long time periods required for self healing to be effective.  For example, the original land disturbances that resulted in the current physical habitat conditions on Libby, Grave, Dunn and Pipe creeks occurred many decades ago, and in the case of Libby and Grave creeks, dates back to the early 1900s.  In each of these potential project areas, the disturbance regimes have been removed for at least 30 years, and yet the habitat has been slow to respond.  In most cases, the reason that the habitat has not yet recovered from the original disturbance is that healthy riparian areas and the large woody debris that recruits from these areas is absent or nonfunctional.  We consider the physical restoration techniques that we utilize to be short-term fixes intended to serve as a stop gap measure until the riparian community reestablishes.  In addition to the physical structures we place in streams to create habitat for salmonids and stabilize the stream banks, we also design the restoration projects to promote the natural functions required to reestablish a healthy riparian plant community that will provide the long-term function and stability.  In some cases we use cultured riparian plant production to further facilitate this process.

b)  The stream restoration work that we completed on the Libby Creek Upper Cleveland Stream Restoration Project in 2002 restored approximately 3,200 feet of stream channel to a dimension, pattern and profile to a stream form that is capable of sustaining its form and function through time.  The project resulted in an overall increase in the quality and quanity of salmonid habitat within the project area, especially pool-type habitat.  Past land management activities including logging, mining, riparian road construction, and stream channel manipulation had resulted in accelerated bank erosion along a number of meander bends, resulting in an over widened, unstable, and shallow channel (Sato 2000), which was contributing to the low quality habitat for native salmonids including bull trout and redband trout.   The existing channel prior to this restoration project was over-widened with frequent lateral migration of the active stream channel.  These conditions resulted in frequent multiple channels within the project reach.  A lack of substantial riparian community further contributed to channel instability.  Prior to project implementation, the width-to-depth ratios were high (ranging from 28-43 feet) and the stream was shallow, with mean bankfull channel depths ranging from 0.58 to 1.79 feet in depth.  We constructed the stream channel, using reference reach criteria established by Rosgen (1996).

The Libby Creek Upper Cleveland Stream Restoration Project was completed in November 2002, after excavating approximately 3,200 feet of new channel according to the design criteria (Dunnigan et al. 2004) including an average design bankfull width and depth of 32 feet and 3 to 7 feet, respectively.  We designed the channel pattern to utilize existing riparian vegetation in project reach wherever possible, in an attempt to maximize channel stability, and promote a more rapid recovery of the riparian area.  The resulting stream pattern design increased sinuosity (stream length divided by valley length) from 1.1 to 1.6, and subsequently increased total stream length from approximately 2,700 to 3,200 feet.  Substantial effort was also expended to restore a healthy riparian vegetative community.  These efforts included transplanting approximately 500 shrubs during construction and planting approximately 2,000 willow cuttings, 75 cottonwood poles, and 1,600 containerized native shrubs after stream channel construction.

The project resulted in an overall narrower and deeper stream channel.  In 1999, prior to project construction, we measured stream channel morphology at 5 cross-sectional survey locations in riffle habitat within the project area.  After project construction in 2002 we established 9 permanent transects in riffle habitats.  These same locations were surveyed again in the summer of 2003, after the project had experienced the first spring freshet.  At each transect we measured mean bankfull width, depth, width to depth ratio, and cross sectional area.  We used analysis of variance (ANOVA) and a subsequent multiple comparison test (Fisher’s Least Significant Difference; Zar 1996) to test for significant differences between years (alpha = 0.05; Table 1).   Mean bankfull width, depth, and width to depth ratio were significantly reduced from 1999 to 2002 and 1999 to 2003.  Comparisons for the three parameters between 2002 and 2003 were not significantly different (p > 0.05; Table 1).  However, the associated variance for each of the 4 parameters decreased each year (Table 1).

Due to the importance of pool habitat to rearing redband and bull trout within the project area, we devoted a substantial effort to monitor pool habitat to evaluate whether our work increased the quantity and quality of pools and whether the pools maintained depth, width and length through time.  The stream channel profile prior to project construction contained few pools (Figure 1), and due to the limited geographical overlap with the newly designed channel thalweg could not accurately be displayed on the same figure as the new channel profile surveyed in 2002 and 2003 (Figure 2).  The designed channel profile required excavation at numerous depositional areas throughout the project reach (Figure 2) and resulted in an increased quantity of pool habitat within the project area.  Prior to project construction, the mean pool-to-pool distance was 325.4 feet.  We resurveyed the project area in the summer of 2003 after the restoration work had been subjected to the first spring freshet after construction, and the mean pool spacing was 172.8 feet, which represented a 223% increase in the total number of pools.   After project construction in the fall of 2002, we measured mean bankfull depth, width, length and maximum bankfull depth of the 20 pools constructed in the project area.  We repeated these measurements in the summer of 2003 after the project had experienced the first spring freshet.  We did not perform a statistical comparison for these data because the pool measurements represented all pools within the project area (i.e. complete census), making statistical comparisons unnecessary.  We observed a decrease in the mean values of each of the 4 parameters from 2002 to 2003 (Table 2).  Mean bankfull depth showed the sharpest decline (18%) from 2002 to 2003, followed by pool length, which decreased by 17.7% (Table 2).  The variance of each of the 4 parameters also decreased from 2002 to 2003 (Table 2).

| Table 1. Mean bankfull width, depth, width to depth ratio and cross sectional area for 5 cross sectional surveys in 1999 and 9 different cross sectional surveys in 2002 and 2003. Variance estimates for annual mean values are presented in parentheses. An analysis of variance (ANOVA) was preformed for each parameter, and the P value is presented for each ANOVA. The results of subsequent multiple comparisons (Fisher’s Least Significant Difference) are also presented (alpha = 0.05). |
| --- |
|  | Mean Bankfull Width (ft) | Mean Bankfull Depth (ft) | Width to Depth Ratio | Cross Sectional Area (Square ft.) |
| 1999 (Pre Restoration) | 41.5 (35.2) | 0.94 (0.07) | 47.6 (359.8) | 39.6 (211.3) |
| 2002 (As Built) | 34.3 (30.5) | 1.33 (0.09) | 26.7 (59.0) | 46.0 (114.3) |
| 2003 | 31.5 (18.5) | 1.48 (0.04) | 21.8 (25.4) | 47.9 (62.5) |
| ANOVA and Multiple Comparison Results | P = 0.008 1999/2002 Significant 1999/2003 Significant 2002/2003 Non-Signif. | P = 0.004 1999/2002 Significant 1999/2003 Significant 2002/2003 Non-Signif. | P = 0.0007 1999/2002 Significant 1999/2003 Significant 2002/2003 Non-Signif. | P = 0.385 1999/2002 Non-Signif. 1999/2003 Non-Signif. 2002/2003 Non-Signif. |

| Table 2. Mean bankfull width, depth, maximum bankfull depth, and length measured from 20 pools in 2002 and 2003. Variance estimates for annual mean values are presented in parentheses. A statistical comparison of annual mean values was not performed because the 20 pools represented all pools within the project area, and therefore represents a complete census. The percent change for each parameter from 2002 to 2003 is also presented. |
| --- |
|  | Mean Bankfull Width (ft) | Mean Bankfull Depth (ft) | Maximum Bankfull Depth (ft) | Length (ft.) |
| 2002 (As Built) | 37.95 (23.75) | 2.64 (0.763) | 4.32 (1.148) | 36.7 (205.2) |
| 2003 | 34.5 (16.07) | 2.16 (0.30) | 3.80 (0.684) | 30.2 (130.8) |
| Percent Change | -9.16% (-32.3%) | -18.01% (60.7%) | -12.03% (-40.4%) | -17.67% (-36.2%) |

Figure 1.  The longitudinal profile of the existing stream channel prior to the implementation of the restoration project.  The survey was conducted beginning at station 0 (upper project boundary) to approximately 2350 feet prior to the implementation of the restoration project in the fall of 2002.  The survey was not completed for the lower approximate third of the project area.  Note the lack of pool habitat within the project area.

Figure 2.  The longitudinal profile of the constructed stream channel thalweg in 2002 (as built) and 2003 after the project experienced the first spring freshet.  The survey begins at the upper project boundary (station 0) and proceeds downstream to the lower project boundary (approximate station 3200).  The stream channel prior to channel construction was not located within the same general plan view as the newly constructed stream channel.  Therefore, the existing stream channel longitudinal profile (Figure 1) could not be superimposed on this figure due to differences in stream channel length that resulted from an overall increase in overall channel sinuosity and length after project construction.

The mean annual variance for mean bankfull depth had the highest decrease (18%) between 2002 and 2003, followed by maximum bankfull depth variance, which decreased by 40.4% (Table 2).  Although mean pool length decreased by 17.7%, the total proportion of pool habitat (sum of all pool lengths divided by total project area stream length) within the project area decreased by 4%, from 22% in 2002 to 18% in 2003.  The changes between 2002 and 2003 were slight, and although some of the dimensions decreased between 2002 and 2003, pool frequency, length, and mean depth were higher than existing conditions prior to the project.

Results demonstrate that the quantity and quality of pool-type habitat and habitat diversity and complexity were limiting factors in this section of Libby Creek prior to restoration activities, and that the restoration project we completed successfully improved rearing conditions for resident salmonids by increasing the depth, available pool quantity and quality and habitat complexity.  Furthermore, these changes have been self- sustaining.  Stream geomorphology, stream habitat, salmonid abundance and standing crop are related and significantly correlated (Kelly et al. 1989; Lanka et al. 1987; Kozel and Hubert 1989).  Muhlfeld et al. (2001a; 2001b) found that redband trout in a third-order tributary to the Kootenai River relied on large complex pools for both summer and overwintering habitat.  Pool habitat has also been identified as critical habitat for cutthroat trout (Schlosser 1991; Irving 1987; Pratt 1984; Dunnigan et al. 1997).  Complex habitat associated with pool-type habitat has also been shown to be an important factor influencing the distribution of bull trout during summer (Pratt 1992) and winter (Thurow 1997, and Bonneau 1994) periods.  Streams that are hydraulically complex as a result of varied and complex habitat have been shown to lose proportionally fewer fish, have fish assemblages that are generally more resilient, and have generally higher fish diversities compared to hydraulically simple streams after floods (Pearsons et al. 1992).  The physical changes to the habitat on Libby Creek as a result of the Libby Creek Upper Cleveland Stream Restoration Project are consistent with conventional scientific principals related to the abundance and distribution of stream dwelling salmonids as they relate to physical habitat conditions.   Therefore, based on the condition of the physical habitat that resulted from the Libby Creek Upper Cleveland Stream Restoration Project (and other similar projects), this effort was a success.  However, the life histories of the fish species inhabiting these streams dictates that they will not sexually mature until age 3-5, and in the case of bull trout, the age at maturity is as long as 5-8 years.  Given this lengthy period of time, it is unreasonable to expect immediate increases in abundance.  We are confident that the physical changes to the habitat will translate into real and substantial increases at the local population level, but that these changes may take many years to realize.  We feel our monitoring components associated with this (and all our projects) will be adequate to detect these changes through time.

References

Bonneau, J. L. 1994. Seasonal habitat use and changes in distribution of juvenile bull trout and cutthroat trout in small, high gradient streams. Master’s of Science Thesis. Moscow: University of Idaho.

Dunnigan, J.L., Bennett, D.H., and Rieman, B.E. 1998. Effects of forest management on westslope cutthroat trout distribution and abundance in the Coeur d’ Alene River system, Idaho, USA. Pages 471-476 in M.K. Brewin and D.M.A. Monita, technical coordinators Forest-fish conference: land management practices affecting aquatic ecosystems.  Procedings Forest-Fish Conference, May 1-4, 1996, Calgary Alberta. Natural resources Canada, Canadian Forest Service. North Forest Centre, Edmonton, Alberta. Information report NOR-X-356.

Dunnigan, J.L, B. Marotz, J. DeShazer, L. Garrow, and T. Ostrowski. 2004. Mitigation for the construction and operation of Libby Dam:  Annual report 2003. Bonneville Power Administration. Portland, Oregon.  Project Number 199500400.

Irving, D. B. 1987. Cutthroat trout abundance, potential yield, and interaction with brook trout in Priest Lake tributaries. Master’s of Science Thesis. Moscow: University of Idaho.

Kelly, M., S. Moore, and S. V. Gregory. 1989. Geomorphic and riparian influences on the distribution and abundance of salmonids in a cascade mountain stream. U.S. Forest Service General Technical Report PSW-110.

Kozel, S. J., and Hubert, W. A. 1989. Testing of habitat assessment models for small trout streams in the Medicine Bow National Forest, Wyoming. North American Journal of Fisheries Management 9:458-464.

Lanka, R. P. Hubert, W. A., and Wesche, T. A. 1987. Relations of geomorpohology to stream habitat and trout standing stock in small Rocky Mountain streams. Transactions of the American Fisheries Society 116:21-28.

Muhlfeld, C. C., D. H. Bennett, and B. Marotz. 2001a. Summer habitat use by Columbia River redband trout in the Kootenai River drainage, Montana. North American Journal of Fisheries Management 21:223-235.

Muhlfeld, C. C., D. H. Bennett, and B. Marotz. 2001b. Fall and winter habitat use and movement  by Columbia River redband trout in a small stream in Montana. North American Journal of Fisheries Management 21:170-177.

Pearsons, T. N., H. W. Li, and G. A. Lamberti. 1992. Influence of habitat complexity on resistance to flooding and resilience to stream fish assemblages. Transactions of the American Fisheries Society 121:427-436.

Pratt, K. L. 1992. A review of bull trout life history. In: Howell, P.J. and Buchanan, D. V. ed. Proceedings of the Gearhart Mountain bull trout workshop. Corvallis: Oregon Chapter of the American Fisheries Society. pp. 5-9.

Pratt, K. L. 1984. Habitat use and species interations of juvenile cutthroat trout (Salmo cclarki lewisi) and bull trout (Salvelinus confluentus) in the upper Flathead River basin. Master’s of Science Thesis. Moscow: University of Idaho.

Schlosser, I. J. 1991. Stream fish ecology: a landscape perspective. Bioscience 41(10):704-712.

Thurow, R. F. 1997. Habitat utilization and diel behavior of juvenile bull trout (Salvelinus confluentus) at the onset of winter.  Ecology of Freshwater Fish 6:1-7.

Zar, J.H.  1996.  Biostatistical analysis.  Third edition.  Prentice-Hall Inc.  Englewood Cliffs, New Jersey.